Contents

| CHAPTER 1 PACKING DETAIL AND INSTALLATION ……………………………. | 6 |
| --- | --- |
| 1-1 Packing ………………………………………………………………………………... | 6 |
| CHAPTER 2 PANEL LOCATION ………………………………………................... | 7 |
| 2-1 Front Panel Controls ………………………………………………………………… | 7 |
| 2-2 Rear Panel Connectors ……………………………………………………………… | 8 |
| CHAPTER 3 SPECIFICATIONS ……………………………………………………….. | 9 |
| CHAPTER 4 LIVE, PLAYBACK AND PTZ OPERATIONS …............................ | 11 |
| 4-1 Live Mode …………………………………………………………………………….. | 11 |
| 4-1.1 Remote Controller ………………………………………………………………….. | 12 |
| 4-1.2 Main Screen OSD …………………………………..…………………………….. | 13 |
| 4-2 Playback Mode ……………………………………………………………………….. | 14 |
| 4-3 PTZ Mode …………………………………………………………………………….. | 15 |
| CHAPTER 5 SETUP YOUR DVR…………..…………………………………………… | 17 |
| 5-1 Record Setup …………………………………………………………………........... | 20 |
| 5-1.1 Quality & Frame Rate Setup …………………………………………………. | 21 |
| 5-2 Event Setup …………………………………………………………………………... | 22 |
| 5-2.1 Motion Setup …………………………………………………………………... | 23 |
| 5-2.1.1 Motion Area Setup …………………………………………………… | 24 |
| 5-2.2 Sensor Setup ………………………………………………………………….. | 25 |
| 5-3 Schedule Setup ………………………………………………………………........... | 26 |
| 5-3.1 Schedule Record Setup ……………………………………………………… | 27 |
| 5-3.2 Holiday Setup …………………………………………………………………. | 27 |
| 5-4 Camera Setup ………………………………………………………………………... | 28 |
| 5-5 Account Setup ………………………………………………………………………... | 30 |
| 5-5.1 Permission Setup ……………………………………………………………… | 31 |
| 5-6 Networking Setup ……………………………………………………………………. | 32 |
| 5-6.1 Networking Setup ……………………………………………………………... | 33 |
| 5-6.1.1 DHCP …………………………………………………………………. | 35 |
| 5-6.1.2 LAN ……………………………………………………………………. | 35 |
| 5-6.1.3 ADSL …………………………………………………………….......... | 36 |
| 5-6.2 HTTP Setup ……………………………………………………………………. | 36 |
| 5-6.3 DDNS Setup …………………………………………………………………… | 37 |
| 5-6.4 Mail Setup ……………………………………………………………………… | 38 |
| 5-7 PTZ & RS485 Setup …………………………………………………………………. | 39 |
| 5-8 System Setup ………………………………………………………………………… | 40 |
| 5-8.1 Display Setup ………………………………………………………………….. | 40 |
| 5-8.2 Date/Time Setup ………………………………………………………………. | 41 |
| 5-8.2.1 Change Date & Time ………………………………………………… | 41 |
| 5-8.2.2 Time Zone Setup …………………………………………………….. | 42 |
| 5-8.2.3 Internet Time Setup ………………………………………………….. | 44 |
| 5-8.3 Buzzer & Relay Setup ………………………………………………………… | 45 |
| 5-8.4 SPOT Setup ……………………………………………………………........... | 46 |
| 5-9 Utility Setup …………………………………………………………………………… | 47 |
| 5-10 Diagnostic …………………………………………………………………………… | 49 |
| CHAPTER 6 BACKUP & SEARCH ………………………………………... | 50 |
| 6-1 Backup Setup ………………………………………………………………………… | 50 |
| 6-2 Search Setup …………………………………………………………………............ | 51 |
| 6-2.1 Event Search ………………………………………………………………….. | 52 |
| 6-2.1.1 Criteria Setup For Event Search ……………………………………. | 53 |
| 6-2.2 Time Search ……………………………………………………………........... | 54 |
| CHAPTER 7 NETWORK SURVEILLANCE ………………………………. | 55 |
| 7-1 IE Setup ……………….……………………………………………………………… | 55 |
| 7-2 Software Installation and Setup ……………………………………….............. | 57 |
| 7-3 Software Operation ……………………………………………………………… | 59 |
| CHAPTER 8 MOBILE APPLICATION INSTALLATION AND USAGE…. | 61 |
| 8-1 Mobile Application Installation and Operation for Symbian System……..……… | 61 |
| 8-1.1 Mobile Application Installation …………………………………………......... | 61 |
| 8-1.2 Mobile Application Operation ………………………………………………… | 61 |
| 8-1.2.1 Add New Login DVR …………………………………………………. | 61 |
| 8-1.2.2 Logging Onto the DVR ………………………………………………. | 62 |
| 8-1.2.3 Modify the Login Information of DVR ………………………………. | 63 |
| 8-1.2.4 Delete the Login Information of DVR ………………………………. | 63 |
| 8-1.3 Live Monitoring Operation ……………………………………………………. | 63 |
| 8-1.3.1 Scroll the Image ……………………………………………………… | 63 |
| 8-1.3.2 Image Quality Setup …………………………………………............ | 64 |
| 8-1.3.3 Channel Display………………………………………………………. | 64 |
| 8-1.3.4 Size of Image …………………………………………………........... | 64 |
| 8-1.3.5 Rotate the Image …………………………………………………….. | 65 |
| 8-1.3.6 Alarm ………………………………………………………………….. | 65 |
| 8-2 Mobile Application Installation and Operation for Windows Mobile System. | 66 |
| 8-2.1 Mobile Application Installation ……………………………………………….. | 66 |
| 8-2.2 Mobile Application Operation ………………………………………………… | 67 |
| 8-2.3 Operation Under The Live Monitoring….……………………………………. | 68 |
| 8-2.3.1 Operation Under The LIVE Monitoring For Jrviewer……………… | 68 |
| 8-2.3.2 Operation Under The LIVE Monitoring For H264 Pocket….…….. | 69 |
| CHAPTER 9 CMS INSTALLATION AND USAGE GUIDE ………………. | 70 |
| 9-1 CMS Installation ……………………………………………………………………… | 70 |
| 9-2 CMS Login and Environment ……………………………………………………….. | 73 |
| 9-3 Setup your own remote surviellance……………………………………………….. | 74 |
| 9-3.1 User Setup ………………………………………………………………………….. | 75 |
| 9-3.2 DVR Connection ……..…………………………………………………………….. | 76 |
| 9-3.3 Group Setup…… ……..…………………………………………………………….. | 77 |
| 9-3.4 eMap Setup…………………………………………………………………………… | 78 |
| 9-4 Remote Surveillance Management ………………………………………………….. | 79 |
| 9-4.1 View a DVR/Group List……………………………………………………………… | 79 |
| 9-4.2 View Event Logs……………………………………………………………………… | 80 |
| 9-4.3 Main Display…………………………………………………………………………… | 80 |
| 9-4.4 Audio Control…………………………………………………………………………… | 81 |
| 9-4.5 eMap Display…………………………………………………………………………… | 81 |
| 9-4.3 PTZ Control…………………………………………………………………………… | 83 |
| 9-5 Local PC Video Record and Information………………………………………….. | 83 |
| 9-6 Playback Video ………………………………………………………………………… | 84 |
| 9-6.1 Remote Play …………………………………………………………………... | 84 |
| 9-6.2 HDD Playback...……………………………………………………………….. | 85 |
| 9-6.3 File Playback ………………………………………………………………….. | 86 |
| 9-6.4 Event Playback………………………………………………………………… | 87 |
| 9-6.5 Snapshot Data .………………………………………………………………... | 88 |
| 9-6.6 Recording Data……………………………………………………………….. | 88 |
| APPENDIX I HARD DISK INSTALLATION ……………………………….. | 89 |
| APPENDIX II TROUBLE SHOOTING …………………………………….. | 91 |

CHAPTER 1 PACKING DETAIL AND INSTALLATION

1-1 PACKING

1. DVR

2. User Manual    3. IR Remote Control      4. Batteries x 2

5. CD              6. Power Adapter              7. Power Cord

8. HDD Screws x 4

CHAPTER 2 PANEL LOCATION

2-1 FRONT PANEL CONTROLS

| Control Keys | Description |
| --- | --- |
| (1) USB 2.0 Port | Port for USB external devices. |
| (2) LED Display | POWER：Power is on. HDD：Hard disk is in use. |
| (3) BACKUP | In LIVE mode, press to display the BACKUP menu. |
| (4) PIP | In LIVE mode, display with picture in picture format. |
| (5) ZOOM | In LIVE or PLAYBACK mode, enlarge the display of a channel. |
| (6) AUTO SEQ. | In LIVE mode, cycle through all channels in full screen. |
| (7) | Display the search menu. |
| (8) ESC | In SETUP mode, press to return to previous page. |
| (9) MENU | In LIVE mode, press to display menu. |
| (10) ● REC | Start or stop recording. |
| (11) ▌▌ PAUSE | In PLAYBACK mode, press to pause playback. |
| (12) ▶ PLAY | Play back in normal speed. |
| (13) ( / (( | In SETUP mode, press to reduce value. In PLAYBACK mode, press to play rewind. |
| (14) ( / (( | In SETUP mode, press to increase value. In PLAYBACK mode press to play forwards. |
| (15) ( / SLOW | In SETUP mode, press to move cursor up. In PLAYBACK mode, press to slow down. |
| (16) ( DOWN/ ■ STOP | In SETUP mode, press to move cursor down. In PLAYBACK mode, press to stop playing back. |
| (17) ENTER/MODE | In SETUP mode, press to enter values. In PLAYBACK mode, switch between full, quad, 9-channel, 16-channel display in order. |

2-2 REAR PANEL CONNECTORS

| (1) VIDEO OUT | BNC output port for the main monitor. |
| --- | --- |
| (2) VIDEO IN | BNC input ports for cameras, 4/8 in total. |
| (3) AUDIO IN | RCA input port for audio signal. |
| (4) AUDIO OUT | RCA output for audio signal. |
| (5) VGA | VGA port. |
| (6) Camera Power | Power for cameras |
| (7) FUNCTION | 1：RS-485 A 2：RS-485 B 3：RELAY NO 4：RELAY COM 5：RELAY NC 6：ALARM IN GND 7：ALAMR IN CH1 | 8：ALARM IN CH2 9：ALARM IN CH3 10：ALARM IN CH4 11：ALARM IN CH5 12：ALARM IN CH6 13：ALARM IN CH7 14：ALARM IN CH8 |
| (8) LAN | Network port. |
| (9) NTSC／PAL SWITCH | Switch between NTSC and PAL format. |
| (10) SPOT MONITOR | BNC port to display full screen image of all installed cameras in sequence. |
| (11) POWER (DC 12V) | Socket for a DC 12V input. |

CHAPTER 3 SPECIFICAITONS

| 1. VIDEO |
| --- |
| Input Level |  | 1.0 Vp-p±10% Composite, 75( Balanced |
| Display Speed | NTSC | 120fps (4CH) |
|  | PAL | 100fps (4CH) |
| Display Resolution | NTSC | 720 x 480 |
|  | PAL | 720 x 576 |
| Monitor Output |  | 2Vp-p Composite, 75( Balanced |
| 2. RECORDING |
| Compression Method |  | H.264 |
| Recording Speed |  | Refer to table 3-1 |
| Recording Resolution | NTSC | 720 x 480, 720 x 240, 352 x 240 |
|  | PAL | 720 x 576, 720 x 288, 352 x 288 |
| Quality | Independent for each channel | Lowest/ Low/ Normal/ High/ Highest |
| Schedule |  | Setup by “minute” as unit |
| Mode |  | Manual∕Event (Motion, Sensor)∕Schedule |
| Method |  | By resolution, fps and quality Setup fps and quality separately for normal and event recording |
| 3. SATA DEVICE |
| Capacity | Internal Storage | 1HDD |
| Type |  | SATA∕SATAⅡ compatible |
| 4. ALARM |
| Sensor Input |  | 4 (4CH) |
| Motion Detection |  | Available per each camera/Multi-detection level |
| 5. CONNECTIONS |
| Video Input |  | BNC 4 ports (4CH) |
| Video Output |  | BNC 1port；VGA 1 port (Option) |
| Audio Input |  | RCA 1CH |
| Audio Output |  | RCA 1 CH |
| USB 2.0 |  | USB memory stick, USB Mouse, USB Touch Panel |
| Remote |  | Standard remote control |
| External I/O |  | 1 RS-485, 4 (4CH) sensor input, 1 Relay Output |
| Ethernet |  | 1 RJ45 connector, 10/100 Mbps |
| 6. ELECTRICAL |
| Power Source |  | DC 12V∕3A above |
| 7. ENVIRONMENTAL |
| Operate Temperature |  | 5℃ ~ + 40℃ |
| Humidity |  | Less than 90% |
| 8. PHYSICAL |
| Dimension |  | 288 (W) x 220 (L) x 58(H) mm |
| Weight |  | 1.8 kg |
| 9. BACKUP |
| BACKUP | USB Stick | Video Data, Audio |
|  | Network | Video Data, Audio |
| 10. SEARCHING & PLAYBACK |
| Searching Method |  | Event∕Time |
| 11. MULTI-REMOTE SURVEILLANCE |
| Monitor Environment |  | Web∕Client Software (CMS) |
| Max. client |  | Supporting multi-client (5 clients accessible) |
| 12. OTHERS |
| OS |  | Embedded Linux |
| Multi Task | Pentaplex | Live、Record、Playback、Network、Data transfer |
| Control Device |  | Front Keys∕Remote Control Virtual Keyboard∕Mouse∕AP Software |
| PC Viewer |  | Direct viewing of DVR’s HDD on PC |
| Numbers of event list |  | 9999 |

Table 3-1

| Recording Speed (Independent setting for each channel) | NTSC | 352 x 240 | 120fps∕4CH |
| --- | --- | --- | --- |
|  |  | 720 x 240 | 60fps∕4CH |
|  |  | 720 x 480 | 30fps∕4CH |
|  | PAL | 352 x 288 | 100fps∕4CH |
|  |  | 720 x 288 | 50fps∕4CH |
|  |  | 720 x 576 | 25fps∕4CH |
| Compression Method | H.264 |

CHAPTER 4 LIVE, PLAYBACK AND PTZ OPERATIONS

The IR remote control and mouse operate differently under each mode; this chapter describes the functions of them under three different modes: LIVE, PLAYBACK and PTZ.

4-1 LIVE MODE

You can monitor all the channels, listen to audio signal and have some related operations under LIVE mode. This paragraph describes the IR remote control, mouse operation and on screen graphical icons under LIVE mode.

4-1.1 REMOTE CONTROLLER

The meaning for each button on the remote control is explained below:

Table 4-1.1 Remote control functions under the LIVE mode

4-1.2 MAIN SCREEN OSD

Table 4-1.2 Graphical icons appeared after right-click on the mouse under LIVE mode.

| Icon | Description | Icon | Description |
| --- | --- | --- | --- |
|  | Setup |  | Pause |
|  | Main Menu |  | PIP, picture in picture |
|  | Search Setup |  | ZOOM, double the screen size |
|  | Backup |  | Auto-Sequence |
|  | PTZ Control |  | LOCK, activate the key lock. |
|  | Record On∕Off |  | Full Screen |
|  | Playback |  | Quad Display |
|  | Display Setup |  |

Table 4-1.3 Description for camera status in LIVE mode

| Icon | Description | Icon | Description |
| --- | --- | --- | --- |
|  | Motion detected on the channel |  | Video loss detected on the channel |
|  | Sensor triggered on the channel | number | No event happening |

Table 4-1.4 Description of on screen graphical icons in LIVE mode

| Icon | Description | Icon | Description |
| --- | --- | --- | --- |
|  | Recording is on |  | Remote user currently logging into DVR |
|  | Audio is on |  | Timer recording is on Red：Timer is set and recording has been started White：Timer is set but recording has not yet been started |
|  | Audio is off |  |  |
|  | USB device detected |  | Auto-Seq is on |
|  | DVD burner is detected | 2X | 2X zoom in is on |
|  | Lock is on |  | Pause is on, screen is frozen |
|  | PTZ control is on |  |  |

4-2 PLAYBACK MODE

Switch to PLAYBACK mode by pressing “PLAY” under the LIVE mode, the graphical icon  will show up on the upper center of the screen and the operation panel (see below picture) will show up at right lower corner of the screen. You can drag the panel by mouse to place it on any location of your screen.

Table 4-2.1 Remote control functions under the PLAYBACK mode

| Button | Description |
| --- | --- |
| ENTER∕MODE | Switch to full screen, quad channel display. |
| MENU∕▌▌ | Turn on∕off PAUSE. |
| PLAY | Play back at normal speed. |
| ▲∕SLOW | Play back at slower speed. The speed will be slowed to 1/2, 1/4, 1/8, 1/16 by each pressing of the button till the slowest limitation of 1/16 of the normal speed. Current playback speed is shown in the upper center of the screen. |
| ▶▶∕▶ | Fast rewind. Each press increases the speed to the next level. There are six speeds: 2x, 4X, 8X, 16X, 32X and 64X. |
| ◀◀∕◀ | Fast forward. Each press increases the speed to the next level. There are six speeds: 2x, 4X, 8X, 16X, 32X and 64X. |
| ▼∕■ | Stop playback. |

Table 4-2.2 Mouse operation under the PLAYBACK mode.

| Icon | Description | Icon | Description |
| --- | --- | --- | --- |
|  | 「◀◀／◀」Fast rewind |  | 「▼／■」, Stop playback |
|  | 「▶▶／▶」Fast forward |  | Playback channel by channel with snap shot display |
| ／ | Play／Pause |  | Full screen display |
|  | 「▲／SLOW」, Slow playback |  | Quad display |

4-3 PTZ MODE

Switch to the PTZ mode by pressing “PTZ” button under the LIVE mode. The PTZ icon  will appear on upper left of the screen but it can be re-located on any place of your screen by dragging the mouse.

Table 4-3.1 Remote Control functions under the PTZ mode

| Button | Description |
| --- | --- |
| ▲／SLOW | Move PTZ up. |
| ▼／■ | Move PTZ down. |
| ◀◀／◀ | Move PTZ to the left. |
| ▶▶／▶ | Move PTZ to the right. |
| ZOOM + | PTZ zoom-in. |
| ZOOM - | PTZ zoom-out. |
| FOCUS + | PTZ focus-in. |
| FOCUS - | PTZ focus-out. |
| IRIS + | PTZ iris-open. |
| IRIS - | PTZ iris-close. |
| TOUR | Activate PTZ pre-set tour. |
| PRESET+ NUMBER | Setup the Preset location; Press “PRESET” key first then two-digit number; DVR will set the current PTZ location at entered preset number. |
| PLAY+ NUMBER | Go to Preset location; Press “PLAY” key first then two-digit number, PTZ will go to the correspondent preset number location. |
| PIP | Set current PTZ location as the start of line-scan. |
| AUTO | Activate AUTO line-scan. |
| ZOOM | Set current PTZ location as the end of line-scan |

Table 4-3.2 Mouse operation under the PTZ mode

| Icon | Description |
| --- | --- |
|  | Leave PTZ Mode, back to the LIVE mode. |
|  | Pre-set number N. (1~64). |
|  | Go to pre-set number N. |
|  | Set current PTZ location at pre-set number N. |
|  | 「TOUR」, press to activate pre-set tour. |
|  | 「PIP」, Set current PTZ location as the start of the line-scan. |
|  | 「FREEZE」, Activate line-scan. |
|  | 「ZOOM」, Set current PTZ location as the end of the line-scan. |
|  | To move PTZ in 360°. |
|  | PTZ zoom in; PTZ zoom out. |
|  | PTZ focus in; PTZ focus out. |
|  | PTZ IRIS open, PTZ IRIS close. |
| Below functions need support from specific PTZ manufacturer. Please check user manual of your PTZ for more detail. |
|  | AUX 1, 「AUTO」key + Number Key「1」 |
|  | AUX 2, 「AUTO」key + Number Key「2」 |
|  | AUX 3, 「AUTO」key + Number Key「3」 |
|  | AUX 4, 「AUTO」key + Number Key「4」 |
|  | AUX 5, 「AUTO」key + Number Key「5」 |
|  | AUX 6, 「AUTO」key + Number Key「6」 |
|  | AUX 7, 「AUTO」key + Number Key「7」 |
|  | AUX 8, 「AUTO」key + Number Key「8」 |
|  | 「Backup」, Customized function. |

CHAPTER 5 SETUP YOUR DVR

Login

To enter the main menu and set up DVR, log-in account and user password are required.

The default password of the administrator is “123456”. Please check the “ACCOUNT SETUP”  for related setup of other log-in users.

Table 5-0.1 Definition of the virtual keyboard.

| Item | Description |
| --- | --- |
|  | Switch between capital and small letters. |
| / | Switch between numbers and letters. |
|  | Press to cancel the setup, and re-choose the login account. |
|  | Delete the last character. |
|  | Enter to identify the password. It will enter the setup menu, if the password is verified. |

Quick Menu

Right click with the mouse, or press the “menu” button on the front panel, and the quick menu will be shown on the display screen. Quick menu provides most common functions for users, eg, playback, full screen display, quad display, etc.

Setup

This provides the setup menu for users. This includes the main menu, for configuration, search setup, backup setup and PTZ setup.

Main Menu

The main menu provides 10 basic setting for DVR. The detail for each basic setup, will be described in the following sections. Note that to start DVR recording, please

(1) go to utility setup and format the HDD and (2) go over recording setup, event setup, as well as schedule setup.

Table 5-0.2 The operation of remote control under the setting menu

| Item | Description |
| --- | --- |
| ( ( | Switch to different options under the one item. |
| (( | Switch to different items. |
| MENU | Save setup and back to LIVE mode. |
| BK-UP∕ESC | Back to Upper level of menu without saving. |
| ENTER | Enter the menu, or display virtual keyboard. |

5-1 RECORD SETUP

Record setup enables the users to enable or disable the recording modes, as well as   the recording quality and frame rate. Please click on the recording modes you wish to enable.

Note that, to enable motion detection, please set “enable” on these functions, as well as to “enable” these function in event setup. For detail, please refer to

Section 5-2.1 on motion detection and Section 5-2.2 for sensor.

Table 5-1.1 The options in record setup

| Item | Description |
| --- | --- |
| HDD FULL | Select STOP to stop recording or OVERWRITE to reuse the HDD when HDD is full 「STOP」：Stop Recording 「OVERWRITE」：Start to overwrite that begin from the oldest data of HDD, and continue to record. |
| RECORD NORMAL | Enable∕Disable normal recording |
| RECORD MOTION | Enable∕Disable recording while Motion is detected |
| RECORD SENSOR | Enable∕Disable recording while Sensor is triggered |
| PRE ALARM RECORD | Enable∕Disable pre-event recording while motion or sensor is triggered but not in the recording mode. The pre-recording time is approximate at 10 seconds (16 MB). |
| AUDIO RECORD | Enable∕Disable Audio recording. |
| QUALITY & FRAME RATE SETUP | Setup the quality and frame rate for each channel under normal recording and event recording type. |

5-1.1 QUALITY & FRAME RATE SETUP

User can adjust the resolution for the cameras. User can also adjust the quality, as well as the frame rate of each individual camera. FPS stands for Frames per second, and as the value increase, the video will be smoother,

Table 5-1.2 The options in quality & frame rate setup

| Item | Description |
| --- | --- |
| RESOLUTION | Choose record resolution from：CIF∕HD1 (2CIF)∕D1. |
| RECORD TYPE | You can setup quality and FPS separately for record type. |
| NO. | Check∕uncheck the box will enable∕disable recording of that channel. |
| QUALITY | Choose from Lowest∕Low∕Normal∕High∕Highest. |
| FPS | Choose recording frame rate. |

5-2 EVENT SETUP

There are two types of events. First is the motion event which detects the movement   in each camera. Second is the alarm event which detects the alarm input from alarm   sensors. Users can adjust the alarm duration (in other word the record time) for the    detected event.

Table 5-2.1 The options in event setup

| Item | Description |
| --- | --- |
| ALARM DURATION (SECONDS) | Set up alarm duration in seconds. Drag the white bar or press ( ( to adjust value. |
| MOTION SETUP | Enter to set up motion detection. |
| SENSOR SETUP | Enter to set up sensor detection. |

5-2.1 MOTION SETUP

Users can enable or disable the functions of motion detection and popup. The cameras can also be setup individually on sensitivity (this means at what level the camera is to determine the movement as a motion), and the region that requires detection.

Note that to use motion detection, you must enable this function here, as well as enable this function in record setup. For detail, please refer to Section 5-1.

Table 5-2.2 The options in motion setup

| Item | Description |
| --- | --- |
| MOTION DETECTION | Check the box to Enable∕Disable Motion Detection for all channels. |
| MOTION POPUP | Check the box to Enable∕Disable popup screen function for all channels. When motion is detected in LIVE mode, the detected channel image will pop up in full screen display. |
| 1~4 | You can setup independently for each channel. |
| SELECTED CHANNEL TURN | Check the box to Enable∕Disable motion detection for each channel. |
| OBJECT SIZE | Drag the white bar or press ( ( to set up Object Size from value 1 to 15 for each channel. The lower value you set the higher sensitivity it will be. Value set up as 1, the motion will be detected easiest. |
| SENSITIVITY | Drag the white bar or press ( ( to set up Sensitivity from value 1 to 15 for each channel. The lower value you set the higher sensitivity it will be |
| MOTION AREA SETUP | Enter to setup motion detection area |

5-2.1.1 MOTION AREA SETUP

The motion area setup allows users to select multiple areas where camera should watch for motion detection. The default area is entire screen. Click and drag the cursor without lifting to mark your selected motion detection area.

Table 5-2.3 The options in motion setup

| Item | Description |
| --- | --- |
| LOCK∕ZOOM | Press LOCK∕ZOOM to select entire screen as detection area. |
| MUTE∕PIP | Press MUTE∕PIP to deselect entire screen as detection area. |
| STATUS | Switch between “SELECT” and “DESELECT” for cursor-dragging function. |
| ENTER | Press to function on the selected area with assigned status. |
| MENU | Press to save the setup and leave. |
| ESC | Press to cancel the setup and leave. |

5-2.2 SENSOR SETUP

This enables or disables the alarm sensor detection and popup. It also determines the  polarity of each alarm sensor.

Note that to use sensor, you must enable this function here, as well as enable

this function in record setup. For detail, please refer to Section 5-1.

Table 5-2.4 The options in sensor setup

| Item | Description |
| --- | --- |
| SENSOR DETECTION | Check the box to Enable∕Disable sensor detection for all channels. |
| SENSOR POPUP | Check the box to Enable∕Disable popup screen function for all channels. When Sensor is detected in LIVE mode, the detected channel image will pop up in full screen display. |
| SENSOR POLARITY | Click or press ▼ to select between HIGH, LOW voltage for triggering sensor detection or OFF to turn off polarity for each channel LOW Polarity：Sensor has not been triggered. When connected, sensor will be turned on. HIGH Polarity：Sensor has been triggered. When connected, sensor status will be turned off. OFF：Sensor is deactivated, and will not be turned on∕off. |

5-3 SCHEDULE SETUP

Setup the schedule is required to command the DVR to record.

Except from starting recording manually, you can also setup the recording time by weeks.The schedule arrangement includes normal, motion detect, and sensor detect recording  type.

It is possible to overlap normal recording, motion recording or alarm recording by setting up several schedules and enable each of the schedules.

Table 5-3.1 The options in schedule setup

| ITEM | DESCRIPTION |
| --- | --- |
| PAGE | Click or press ▼ to select Page. Each page provides 10 schedules for setup. 5 pages in total. |
| SCHEDULE | To enable each schedule, please mark on them. To adjust the content of each scheduling, please click on the option. (See 5-3.1) |
| HOLIDAY SETUP | Enter to setup holiday, up to 50 days, other than weekends. (See 5-3.2) |
| VIEW EVENT SETUP | View Normal/ Motion / Sensor Setup |

5-3.1 SCHEDULE RECORD SETUP

Click on the time on the left side. The setup menu will be displayed. You can have detail setup by Dates, Time and Event.

5-3.2 HOLIDAY SETUP

Since holidays are different by different country and region, you can setup the holiday of your location accordingly.

5-4 CAMERA SETUP

The camera setup can adjust the display and volume for each individual camera.

Table 5-4.1 The options in camera setup

| Item | Description |
| --- | --- |
| 1~4 | You can setup independently for each channel. |
| MASK | Check the box to Enable∕Disable mask function for LIVE mode |
| BRIGHTNESS | Drag the white bar or press ( ( to adjust Brightness of your camera from value 1 to 255. The default value is 128. |
| CONTRAST | Drag the white bar or press ( ( to adjust Contrast of your camera from value 1 to 255. The default value is 128. |
| SATURATION | Drag the white bar or press ( ( to adjust Saturation of your camera from value 1 to 255. The default value is 128. |
| HUE | Drag the white bar or press ( ( to adjust Hue of your camera from value 1 to 255. The default value is 128. (This function doesn’t support at PAL system.) |
| NAME | Set up name of each channel |
| VOLUME | Select to adjust Volume in live mode for CH1 to CH 4 under LIVE mode and recording mode. |

5-5 ACCOUNT SETUP

The Account Setup menu is used to provide role-based permission independently setting for each user (maximum of 4 users) to access DVR over network. The default admin account is「admin」and password is “123456”. You can register new accounts for users by setup   user name, password, permission list, and remember to click on the No. to activate the account,

Table 5-5.1 The options in account setup

| Item | Description |
| --- | --- |
| AUTO LOCK | Function Setting | Auto Logout | Key Lock |
|  | Key lock | ○ | ○ |
|  | Key unlock | ○ | X |
|  | Disable | X | X |
| NO. | Check to activate the user’s account. |
| PASSWORD | Enter to set up password for each user. Password can be set up to 8 characters mixed by letters and numbers with case-sensitive. |
| PERMISSIONS | Enter to set up Permissions for each user. |
| CHANGE ADMIN PASSWORD | Enter to change administrator’s password |

P.s.1：When logged out automatically, you will have to operate in limited authority such as operations like: Freeze the screen, Picture in picture, Zoom in∕out, switch between channels…etc. If you need to enter the Setup menu, Search menu, backup menu, Record…etc, user’s account and password are required.

P.s.2：When the key lock automatically, remote control and mouse can’t function before entering verified password.

P.s.3：「○」: Enable the function, 「X」: Disable the function

5-5.1 PERMISSION SETUP

The Account Setup is set to provide individual user (maximum of 4 users) role-based permissions, including access to Setup menu, Network operation, PTZ function, Playback, Utility, Backup and Mask on specific channels while playing back.

5-6 NETWORKING SETUP

In the networking setup, the user is required to determine the network type of the      network used, and the configurations for it. Users can also setup the HTTP server for   Internet Explorer connection, setup DDNS for the usage of DDNS, and setup mail     server for email notification.

Table 5-6.1 The options in networking setup

| Item | Description |
| --- | --- |
| CONNECT TYPE | Setup mode for network connection：DHCP、LAN、ADSL. |
| HTTP SETUP | Enter to set up HTTP for remote access into DVR. |
| DDNS SETUP | Enter to Enable∕Disable DDNS function and set up. |
| MAIL SETUP | Enter to enable∕disable Email notification and setup. There are up to 10 email addresses can be notified with different event options. |

5-6.1 NETWORKING SETUP

The DVR supports DHCP, LAN and ADSL accesses for network connection. If the settings are subsequently changed, pressing “PLAY” button to drive new settings for re-connection is required.

LAN - STATIC IP

Public Static IP Connection

Private / Virtual IP Static IP Connection

Static IP is considered as a fixed IP assigned by ISP (Public IP) or IP share device (Virtual IP). DVR connecting to static IP needs to be assigned IP address, Gateway, and Subnet mask.

DHCP

The DHCP functions needs to be supported by a router or a cable modem network with DHCP services. It is preferable to use DDNS at DHCP connection. Note that port mapping is required if needed to connect the DVR outside the LAN.

ADSL

The ADSL function needs to have one “username” and one “password” subscribed from one ISP supplier. Please set up username and password for ADSL connection.

5-6.1.1 DHCP

If the DHCP option is used for DVR network connection, an IP address is assigned by the DHCP server automatically.

5-6.1.2 LAN

For LAN option, please select LAN for network connection, and the following information, including IP address, Subnet Mask, Gateway and DNS, is required.

Table 5-6.2 The options in LAN setup

| Item | Description |
| --- | --- |
| IP ADDRESS | Enter IP address provided by ISP |
| SUBNET MASK | Enter IP address of Subnet Mask provided by ISP |
| GATEWAY | Enter IP address of Gate way provided by ISP |
| DNS | Enter DNS address provided by ISP. (Note：The correct DNS address must be entered for DDNS function). |

5-6.1.3 ADSL

Select ADSL for network connection, the following information, including username and password, is required.

Table 5-6.3 The options in ADSL setup

| Item | Description |
| --- | --- |
| USER NAME | Enter user name provided by ISP |
| PASSWORD | Enter password provided by ISP |

5-6.2 HTTP SETUP

To enable IE to connect to the DVR, user is required to enable HTTP server. The      default port for IE is 80.

Table 5-6.4 The options in HTTP setup

| Item | Description |
| --- | --- |
| ENABLE HTTP SERVER | Check to enable HTTP server. Users can remotely access into the DVR over the network if the HTTP function is activated. |
| PORT | Enter a valid port value from 1 up to 65000. The default value is 80. |

5-6.3 DDNS SETUP

To use DDNS, please enable the DDNS function, and choose the DDNS server that is used.

Table 5-6.5 The options in DDNS setup

| Item | Description |
| --- | --- |
| ENABLE DDNS | Check∕Uncheck to enable∕disable DDNS function. |
| DDNS SERVER | Enter the registered SMTP Server： DYNDNS.ORG、NO-IP.ORG、CUSTOM.COM |
| SMTP SERVER | Enter the registered SMTP Server. |
| USER NAME | Enter user name. |
| PASSWORD | Enter password. |

5-6.4 MAIL SETUP

E-mail can be used as a form of notification when an event occurs (VLOSS, MOTION, SENSOR). Please enable e-mail notification to use this function, and fill in related information, including the SMTP server, username, password and email of the sender, as well as the receiver’s email.

Table 5-6.6 The options in mail setup

| Item | Description |
| --- | --- |
| ENABLE E-MAIL NOTIFICATION | Check the box to enable∕disable E-mal Notification function. |
| SMTP SERVER | Enter to set up SMTP Serve name. |
| USER NAME | Enter to set up User Name. |
| PASSWORD | Enter to set up Password. |
| SENDER E-MAIL | Enter to set up e-mail address of sender. |
| E-MAIL ADDRESS | Enter to set up e-mail addresses for up to 10 receivers individually. |
| TRIGGER EVENT | Enter to select events to send out E-mail notifications when below circumstances happen：Motion, Sensor and Vloss (Video Loss). |

5-7 PTZ & RS485 SETUP

The DVR allows users to control PTZ functions of your camera. To enable PTZ function, the 485 cable should be connected to the RS-485 port of DVR.

Table 5-7.1 The options in PTZ and RS485 setup

| Item | Description |
| --- | --- |
| ENABLE PTZ | Click the box to Enable∕Disable PTZ function for each channel. |
| PROTOCOL | Set up the protocol of PTZ cam. The supported protocol are PELCO-P, PELCO-D, KND, LI-LIN. |
| PTZ ID | Click or press ( ( to set up PTZ ID. The valid ID value is from 1 to 64. |
| BAUD RATE | Select Baud Rate for PTZ from 2400、4800、9600 |

5-8 SYSTEM SETUP

The system setup provides basic settings, including (1) OSD display, (2) Date and time, (3) Buzzer, (4) Language, and others.

Table 5-8.1 The options in system setup

| Item | Description |
| --- | --- |
| DVR NAME | The name of DVR will be shown when users login from remote access. |
| DVR LOCATION | The location of DVR will be shown when users login from remote access. |
| LANGUAGE | Click or press ▼ to select OSD language from English, Chinese, Greek, Italian, Japanese, Portuguese, Spanish, German, French, Russian or Polish. |
| AUTO-SEQ. INTERVAL ( SECONDS) | Click or press ( ( to setup duration time in seconds for the interval between channels under Auto-Seq. mode. |
| REMOTE ID | The default Remote ID is 0, when DVR is controlled by standard remote controller. |
| DISPLAY SETUP | Enter to setup Display |
| DATE/TIME SETUP | Enter to setup Date/Time |
| BUZZER & RELAY SETUP | Enter to setup Buzzer & Relay |
| SPOT SETUP | Enter to setup Spot |

5-8.1 DISPLAY SETUP

| Item | Description |
| --- | --- |
| OSD | Turn On∕Off OSD display |
| DVR STATUS | Turn On∕Off DVR illustration and record status display |
| DATE/TIME | Turn On∕Off date and time display |
| MESSAGE | Turn On∕Off message display |
| CHANNEL NAME | Turn On∕Off channel name display |
| BORDER SET | Set up the color of border in LIVE1, PLAYBACK mode.（black、dark grey、light grey、white） |

5-8.2 DATE/TIME SETUP

This provides retrieving the time from Internet, and adjustments for the time zone, date and time.

Table 5-8.3 The options in date/time setup

| Item | Description |
| --- | --- |
| HOUR FORMAT | 12HOURS∕24HOURS |
| DATE FORMAT | MM-DD-YY∕DD-MM-YY∕YY-MM-DD |
| DATE/TIME POSITION | Choose the position of Time and Date display |
| CHANGE DATE & TIME | Setup time and date of DVR |
| TIME ZONE SETUP | Setup GMT and Daylight Saving Time. |
| INTERNET TIME SETUP | Setup automatic synchronization with internet server |

5-8.2.1 CHANGE DATE & TIME

Users are allowed to setup date and time of DVR manually according to your local time.

5-8.2.2 TIME ZONE SETUP

In time zone setup, users can change your time zone and activate Daylight Saving Time function according to your DVR location.

Table 5-8.4 The options in time zone setup

| Item | Description |
| --- | --- |
| SELECT TIME ZONE | Enter to modify GMT from GMT- 13 to GMT+ 13 |
| DAYLIGHT SAVING TIME | Turn on∕off Daylight Saving Time |

5-8.2.3 INTERNET TIME SETUP

Synchronize your DVR time with internet time server.

Table 5-8.5 The options in internet time setup

| Item | Description |
| --- | --- |
| AUTOMATIC SYNCHRONIZATION | Check to enable DVR automatic synchronization function. Effective by this option selected, DVR will automatically synchronize the time upon rebooting or by every 24 hours after booting. |
| UPDATE NOW | Effectively, Date and Time show on DVR will immediately correspond with those in internet server. |

5-8.3 BUZZER & RELAY SETUP

Table 5-8.6 The options in buzzer & relay setup

| Item | Description |
| --- | --- |
| KEY TONE | Enable∕Disable keystrokes. |
| RELAY SWITCH CONNECTION | Set relay signal to be Normal Close (N.C.) or Normal Open (N.O.). |
| BUZZER DURATION | Set up the duration from 1~999 seconds. |
| ALARM BUZZER | Enable∕Disable buzzer operation when the alarm is triggered for sensor, motion and Vloss (Video Loss). |
| ALARM RELAY | Enable∕Disable the signal to be sent to the RELAY OUT blocks when the alarm is triggered for sensor, motion and Vloss. |

5-8.4 SPOT SETUP

The DVR has two modes of video output; one is main video output, the other is spot video output. SPOT setup is for controlling the order of channels the system cycles through in SPOT mode. User can monitor every channel in the SPOT mode.

Table 5-8.7 The options in buzzer & relay setup

| Item | Description |
| --- | --- |
| SPOT MODE | Channels display in spot for three different modes： MANUAL：Select channels to display manually. SEQUENCE：Auto-sequence for all channels in order. EVENT：Display channels with event occurred. |
| INTERVAL (SECONDS) | The duration time in seconds for the interval between channels under SPOT mode. |
| SKIP VIDEO LOSS CHANNEL | Whether to skip channels without video signal. |

5-9 UTILITY SETUP

This is used to reset or upgrade the system, including the HDD, DVR, USB device.

Table 5-9.1 The options in utility setup

| Item | Description |
| --- | --- |
| HDD INITIALIZATION | Select to enter initialize hard disk menu. Please stop recording before entering this menu. Enter the menu, system will show all the data (model, volume) of HDD that installed in DVR. Check the HDD you’d like to initialize then press “START”. HDD initialization is succeeded when the status shows “SUCCEED” |
| USB INITIALIZATION | Clean up all data on USB. Enter USB initialization and press YES to clean up all data on your USB. The initialization is done when it’s showed “SUCCEED”. |
| SYSTEM RECOVERY | Restore system default values |
| RESET SYSTEM EVENTS | Reset all the recording events in DVR. |
| COPY SETUP TO USB | Copy configuration to a USB device. There will be a file named “sdvr.config” on your USB. |
| DOWNLOAD SETUP FROM USB | Download configuration from a USB device into DVR. |
| UPGRADE | Upgrade DVR through USB. Please stop recording and backup setup configuration before upgrading. System will reboot automatically when the upgrade is completed. |

Notice！DO NOT TURN OFF POWER OR UNPLUG USB DEVICE DURING THE UPGRADE as it may cause incomplete firmware upgrade and damage to the DVR.

5-10 DIAGNOSTIC

This shows the DVR, HDD and network information.

Table 5-10.1 The options in diagnosis setup

| Item | Description |
| --- | --- |
| VERSION | The current firmware version of DVR |
| IP ADDRESS | The connected IP address of DVR. If disconnected from network, the screen will display “NETWORK DISCONNECT”. |
| MAC ADDRESS | MAC Address of DVR |
| HDD VOLUME | The capacity of HDD |
| HDD USED RATE | Percentage of space used on HDD. |
| HDD STATUS | Shows HDD status. USING means the HDD is being used for recording now GOOD/BAD means the HDD has a known/unknown format for the DVR. (Note: Please initialize your newly-installed HDD before using it, otherwise it can be recognized as BAD by DVR.) |
| FORMAT TIME | The latest format time of HDD |

CHAPTER 6 BACKUP & SEARCH

To enter the backup or search menu, please find “setup” from the quick menu, and press “backup” or “search”.

6-1 BACKUP SETUP

User can backup any segment of recorded data in a specified time frame. To do so, either a DVD-R/W or storage device, like USB, must be connected to the DVR. The format of backup file is IRF file that can be played by “DVRemoteDesktop.exe” or “iCMS”

Table 6-1.1 The options in backup setup

| Item | Description |
| --- | --- |
| FROM | The start time of backup file |
| TO | The end time of backup file |
| DEVICE | Select USB or DVD-RW as the backup device |
| FREE SPACE | The available space in your backup device |
| REFRESH | Recalculate the available space of backup device |
| CALCULATE | Calculate the size of backup file |
| START | Start backup operation. Be sure to calculate the size of backup file BEFORE operating backup. |

Notice！Do not unplug the USB device or turn off the DVR during the backup process  to avoid unrecoverable error.

6-2 SEARCH SETUP

There are two types of search, event search and time search. In event search, every   event will be shown as a list, and user can choose to playback a certain event. In time search, the user can specify a certain time range to playback.

Table 6-2.1 The options in search setup

| Item | Description |
| --- | --- |
| EVENT SEARCH | Press to enter event search menu |
| TIME SEARCH | Press to enter time search menu |

6-2.1 EVENT SEARCH

The DVR automatically records events with type, time and channel information included. If there is recording data for an event, the recording signal  will be shown on the left side of time information. Rest your cursor under the line and press “ENTER”, or left click your mouse to playback the recording data.

| Item | Description |
| --- | --- |
| CRITERIA | Setup conditions of event search |
| PAGE | Convert pages of events |
| DATE/TIME | Date/time when event occurred. |
| EVENT TYPE | Event type, defined as following |
|  | VLOSS | Video Loss |
|  | MOTION | Motion Detected |
|  | SENSOR | Sensor Detected |
|  | REMOTEIN | user log-in over the network |
|  | REMOTEOUT | user log-out over the network |
|  | POWER ON | System Rebooting |
|  | KEY LOCK | System key are locked |
|  | KEY UNLOCK | System key are unlocked |
|  | HDD FULL | HDD is FULL |
| CHANNEL | The channel where event occurred. |

6-2.1.1 CRITERIA SETUP FOR EVENT SEARCH

The amount of events can be numerous. Therefore, you can facilitate event sorting by setting up “CRITERIA”. Setup “START TIME” and “END TIME” for event search, then the search result will be limited to this specific period of time. Only checked events and channels will be sorted in event search as well.

6-2.2 TIME SEARCH

TIME SEARCH can search for the specific time of recording data to playback. To specify a date, use ◀ or ▶ to move the cursor up and down, use ▲▼ or roll the mouse	to change dates. Press “ENTER” or left click on the desired date to playback. Note that dates with recording data are marked with a red square “ □ “ System will start playing back according to the date you selected. Calendar will be shown by using mouse to click on “YEAR” and “MONTH”.

Click “date” to display recording time of that specific date with time bar. You can change time (hour∕minute∕second) or click on a specific time of time bar by mouse then press “YES”. DVR will playback the selected recording data.

CHAPTER 7 NETWORK SURVEILLANCE

7-1 IE SETUP

Step One：Enter the IP address of DVR in IE browser. Here you may choose to setup

IE remote or download the AP software.

Step Two：Click OK when window prompts to install an ActiveX for IE remote desktop. After Installation, please enter the user name and password. Default user name is

admin and password is 123456. Other related setup about user account and password, please check “5-5 ACCOUNT SETUP“.

Step Three：Please enter information of login DVR: IP, Port, Username and Password,

or choose “PLAY RECORDED FILE” to open backup files in your PC.

Step Four：You’ve logged into the DVR

7-2 SOFTWARE INSTALLATION AND SETUP

The software:「DVR Remote Desktop」can allow you to remotely access and control the DVR from PC.

Step One：Enter the IP address of DVR in IE browser.

Note：This IP is only for reference. Please setup your local IP.

Step Two：Below windows will be shown up. Please enter the user name and password. Default user name is admin and password is 123456. Other related setup about user account and password, please check “5-5 ACCOUNT SETUP“.

Step Three：Click on the link to start downloading the software.

Step Four：Run or Save our software.

Step Five：If you choose to run the software, Start window will be shown up. Please enter information of login DVR: IP, Port, Username and Password, or choose “Play Recorded File” to open backup files in your PC.

Step Six：You’ve logged into the DVR

7-3 SOFTWARE OPERATION

Open the file “DVRemoteDesktop.exe”; enter the information of DVR “IP ADDRESS”, “PORT” “USERNAME” and “PASSWORD” and click “OK”. You should be able to login DVR successfully and start to use the software. The default username and password is 「admin/ 123456」

The operation of software remains the same as local DVR. The user can right-click on the   DVR Remote Desktop.and the main menu will be shown on the screen. The menu    works exactly the same as the one in DVR. (Please refer to Chapter 5 for detail)

Furthermore, it provides some exclusive functions for remote users. Please check       Table 7-3.1 for detail information and Table 7-3.2 for system requirements for software.

Table 7-3.1 Toolbar of AP software

| FILE - RECORD TO LOCAL | Record data to your PC, including LIVE and Playback. |
| --- | --- |
| FILE - PLAY RECORDED FILES | Play recorded files “.irf” |
| FILE – EXIT∕ALT + F4 | Close the AP software. |
| EDIT - CHANNEL NAME∕F2 | Edit channel name of your DVR including font, size italic, and boldface of characters. |
| EDIT - RESET CHANNEL NAME | Reset channel name back to default. |
| VIEW - HIDE CAPTION & MENU∕F9 | Hide the Caption and Menu. |
| VIEW - DISABLE RESIZING∕F10 | Disable resizing the window. |
| VIEW - FULL SCREEN∕F11 | Switch it to full screen. |
| HELP – ABOUT | Show information about software and information. |

Table 7-3.2 System Requirements for AP software

| CPU | Intel Pentium 4 above |
| --- | --- |
| OS | Microsoft Windows Vista、Windows XP SP2 above |
| RAM | 512M above |
| OTHERS | DirectX 9.0 above |

CHAPTER 8 MOBILE APPLICATION INSTALLATION AND USAGE

You can remotely monitor all channels of DVR through your mobile device. The required mobile application is from DVR manufacturer and it supports mobile OS for both Windows mobile 5.0 above and Symbian.

Please confirm network function of DVR has been activated before mobile connection：

Main menu ( Network Setup ( HTTP Setup ( Check the “ENABLE HTTP SERVER”

8-1 MOBILE APPLICATION INSTALLATION & OPERATION FOR SYMBIAN SYSTEM

Mobile Device：Nokia, SonyEricsson…etc.

System requirement：

- GPRS/3G must be provided from your telecom service.

- Mobile device should be support GPRS/3G protocol and Java cldc1.0/midp 2.0 environment.

8-1.1 MOBILE APPLICATION INSTALLATION

Please follow the steps cited below to perform the mobile device surveillance function.

Step 1：The application can be downloaded directly from the manufacturer’s website to your mobile OR; alternatively, it can be transferred to your mobile device from the CD that packed with DVR through Bluetooth or USB cable.

Step 2：Install the application software in your mobile device. It might be installed automatically after downloading; otherwise, select it from the downloading file for installation.

8-1.2 MOBILE APPLICATION OPERATION

After the installation, enter the Program Files menu in

your mobile device to run a file called “H.264 MIDlet”.

Select “MENU” at the right lower corner of your mobile

screen, 4 commands, Login Add Modify and Delete,

will show up.

8-1.2.1 ADD NEW LOGIN DVR

To log into the DVR, you need to enter the logging-in

DVR information. Find “ADD” under the “MENU” then

enter logging-in DVR’s IP address, Port number,

account name and password. Press “ADD” to save this

information after entering.

8-1.2.2 LOGGING ONTO THE DVR

- Use the Login command to log onto a DVR and

Monitor live images. If multiple DVRs have been

added to the mobile application, they will be listed

by name, you can select one to log onto.

- A confirmation message might show up for network

charge before connection. The fee rate will depend

on the telecom company and package fee you go

with.

- Network connectivity will take some time.

It’ll be affected by networking environment and

bandwidth flow.

Live image will show up after a successful connection.

PS. The Live cannot be displayed in your mobile

when the recording is off in local DVR.

8-1.2.3 MODIFY THE LOGIN INFORMATION OF DVR

You can use the “MODIFY” command to change the login information of DVR. The dialogue is identical to that of the “ADD” command.

8-1.2.4 DELETE THE LOGIN INFORMATION OF DVR

“DELETE” command can be used to remove the DVR information if it is no longer useful. Select the DVR on the name list then choose “DELETE”

8-1.3 LIVE MONITORING OPERATION

This paragraph describes some operation under the LIVE monitoring mode in your mobile device.

8-1.3.1 SCROLL THE IMAGE

You can use the keypad on your mobile device to scroll the image if it’s oversized.

| KEY | ACTION |
| --- | --- |
| 2 | Scroll Up |
| 4 | Scroll Left |
| 6 | Scroll Right |
| 8 | Scroll Down |

8-1.3.2 IMAGE QUALITY SETUP

Select “QUALITY” under the “MENU”

There will be 5 levels for \your to choose：

Low、Normal、Middle、High and Highest.

8-1.3.3 CHANNEL DISPLAY

You can choose single or quad channel display for live monitoring.

Select “SINGLE” under the “MENU”, there will be all channels of your DVR in list for you to choose.

PS. The Live cannot be displayed in your mobile

when the recording is off in local DVR.

8-1.3.4 SIZE OF IMAGE

The screen size of different mobile device can be really different. You can select “SIZE” under the “MENU” to choose from “ORIGINAL” or “FIT SCREEN” to resize

the display image.

| Item | Description |
| --- | --- |
| ORIGINAL | The image will be shown in original size. |
| FIT SCREEN | The image will be shown to fit the screen. |

8-1.3.5 ROTATE THE IMAGE

The Live image can be displayed in normal or rotate to 90 degrees. Select “ROTATE” under the “MENU” for this operation.

8-1.3.6 ALARM

This application not only allows you to remotely monitor through mobile device but receive the alarm that has been triggered by events such as Motion Detected, Sensor Triggered and Vloss.

Graphical icons below will be shown on the status：

：Motion detected

：Sensor triggered

：Video loss

Select the “ALARM” under the “MENU” to switch this function on or off.

8-2 MOBILE APPLICATION INSTALLATION & OPERATION FOR WINDOWS

MOBILE SYSTEM

There are two kinds of applications for Window Mobile OS: JPEG compression and H.264 compression. The one for H.264 compression can transfer both audio and video signal to your mobile device.

System Requirement：

Mobile device OS：Windows mobile system 5.0 above.

Mobile device need to support internet: GPRS／3G／Wifi… etc.

8-2.1 MOBILE APPLICATION INSTALLATION

Please follow the steps cited below to perform the mobile

device surveillance function on your mobile device

(mobile phone, PDA...etc).

Step 1：The mobile application called “Jrviewer”

and “H264Pocket.CAB” need to be installed in

your mobile device. The application can be

downloaded directly from the manufacturer’s

website to your mobile or; alternatively, it can

be transferred to your mobile device from the

CD that packed with DVR through Bluetooth

or USB cable.

Step 2：Install the application software “Jrviewer”

and “H264Pocket.CAB” in your mobile device, two folders named ”Jrviewer” and “H264Pocket” will be created. It might be installed automatically after downloading; otherwise, select it from the downloading file for installation.

8-2.2 MOBILE APPLICATION OPERATION

After the installation, enter the Program Files menu in your mobile device to run files named “Jrviewer” and “H264Pocket”.

This application allows you to remotely logon and monitor DVR. Press “OK” to bring up the operation menu; see below chart to further information.

| Item | Function | Description |
| --- | --- | --- |
| ADD | Add login DVR | Enter DVR’s name, IP address, Port, Account user, Password then press “OK” |
| LOGIN | Logon DVR | Choose the DVR that you’d like to log on, then press “OK”. PS. The Live cannot be displayed in your mobile when the recoding is off. PS. Network connectivity will be affected by networking environment and bandwidth flow. The fee rate will depend on the telecom company and package fee you go with. |
| MODIFY | Modify Login DVR | Choose DVR, press “MODIFY”, and press ”OK” to save change. |
| DELETE | Delete Login DVR | Choose DVR and press ”DELETE” to delete the DVR info. |

8-2.3 OPERATION UNDER THE LIVE MONITORING

After successful logon the DVR, press “VIEW” to bring up operation menu. You can choose the channel, resize the image, choose the quality, and turn on/off the status bar, alarm, full screen display….etc.

8-2.3.1 OPERATION UNDER THE LIVE MONITORING FOR JRVIEWER

| Item | Function | Description |
| --- | --- | --- |
| CHANNEL 1~4 | Display for CH 1~4 | Choose from CH 1~4 to display |
| SCREEN | Size of image | Original：image size as original Stretch：stretch the size as full screen Fit：resize the image to fit the screen |
| QUALITY | Quality | Change the quality of image. Please note the better quality, the slower data transfer rate. |
| STATUS BAR | Status Bar | Graphical icons indicated below will be shown on the status bar if there is event such as motion detected, sensor triggered and video loss to be detected on any channel. You can also uncheck the “STATUS BAR” to inactivate this function. Icon Description Motion Detect Sensor Trigger V-Loss |
| ALARM | Alarm | Alarm through your mobile device can be triggered if there is event to be detected. You can also uncheck the “ALARM” under the “VIEW” to inactivate this function. |

8-2.3.2 OPERATION UNDER THE LIVE MONITORING FOR H.264 POCKET

| Item | Function | Description |
| --- | --- | --- |
| CHANEEL 1~4 | Display for CH 1~4 | Choose from CH 1~4 to display. One of channel can receive audio signal. |
| STATUS BAR | Status Bar | Graphical icons indicated below will be shown on the status bar if there is event such as motion detected, sensor triggered and video loss to be detected on any channel. You can also uncheck the “STATUS BAR” to inactivate this function. Icon Description Motion Detect Sensor Trigger V-Loss |
| ALARM | Alarm | Alarm through your mobile device can be triggered if there is event to be detected. You can also uncheck the “ALARM” under the “VIEW” to inactivate this function. |
| FULL SCREEN | Full screen display | You can choose one channel to display in full screen by check this function. |

CHAPTER 9 CMS INSTALLATION AND USAGE GUIDE

CMS stands for Central Management System, which is a software that can manage up

to 4 DVRs through network. Please install the software to start. The following sections

will guide you to prepare your CMS environment.

9.1 CMS installation – Teach you how to install the CMS into your PC.

9.2 CMS login and environment – Teach you how to login, and briefly introduce the software interface.

9.3 ~ 9.5 – Introduce the environment

9-1 CMS INSTALLATION

Please check if your PC reach the following requirements, to make sure it works

properly.

- Intel Pentium 4 processor or equivalent.

- Microsoft Windows Vista、Windows XP、Windows 2003 Server.

- 512MB memory above. (500M requested for group DVR connection and 180M for single DVR)

- 20MB HD space. Recording and image capturing require extra space for storage.

The Installation Instruction

- Open the CD provided in the package and execute “SETUP.EXE”.When the below 	window appear, select “NEXT”.

- Select “BROWSE” to change installation path if needed. To check available space on hard disk, please select “DISK COST”, then please select “NEXT” to go to the next step.

- The ”CONFIRM INSTALLATION” window showsup . Select “NEXT” and the

installation starts.

- Select “CLOSE” to finish installation when the “INSTALLATION COMPLETE” window shows.

9-2 CMS LOGIN AND ENVIRONMENT

To enter CMS, the administrator’s user name and password are entered. The defaults are ‘‘admin’’ and ‘‘123456’’.

After successfully login, the following image shows on your screen:

| (1) OPERATION BAR | A set of 10 operations are provided by CMS. See “9-3 SETUP YOUR REMOTE SURVEILLANCE” and “9-7 PLAYBACK RECORDED VIDEO” for detail. |
| --- | --- |
| (2) DVRS, GROUPS & EVENTS | Information about DVRs, groups and events. See “9-4 REMOTE SURVEILLANCE MANAGEMENT” for detail. |
| (3) MAIN DISPLAY | Live image display area. See“9-4 REMOTE SURVEILLANCE MANAGEMENT” for detail. |
| (4) PC INFORMATION AND CONTROL | Information about local PC’s hard disk, volume, recording...etc. See “9-5 LOCAL PC INFORMATION AND CONTROL” for more detail. |
| (5) DISPLAY MODES | Display modes supported by CMS. Note that group setup is required to use the display modes. See “9-3 SETUP YOUR REMOTE SURVEILLANCE” for detail. |

You need to setup the environment in able startup your remote surveillance. The

setup flow is discussed in Section 9-3.

9-3 SETUP YOUR OWN REMOTE SURVEILLANCE

To setup your own remote surveillance, you have to do 4 things.

(1) 	Determine the user.

If you are the only user, you can use the administrator account. If there are other users, and they are not allowed certain actions, it is preferable to setup an account for each user. To setup a user, please refer to 9-3.1.

(2) 	Connect to your DVR.

You need to setup the network configuration for each DVR, so CMS can reach the 	DVR. Note that an individual setup is needed for each user for each DVR. To		connect to DVR, please refer to 9-3.2.

(3)	Group up your DVRs and arrange the cameras

Assume you have one or more DVRs connected. You can arrange your cameras 	on a specific channel on the screen, and save this arrangement as a group 		name. In this way, you can manage the cameras very easily. For detail, please 		refer to 9-3.3.

(4)	Including additional information

If you want to include a map or some reference information, that is shown as a 		jpeg file, you can use the eMap function to help you reach this goal. For detail, 		please refer to 9-3.4.

When all the above is done, congratulations to you, for you have complete the easy	  setup.

The operations are listed below：

9-3.1 USER SETUP

Before the CMS can be used on a PC, a user accounts should be added with proper authority. Each user should also be assigned a password and optionally a description. If a user does not have certain authority assigned, he/she will not be able to operate the corresponding function on the Operation Bar. The default is none of the authority is assigned. The administrator should assign proper authority to each user. These user accounts can be deleted or edited later on.

Select “OK” to save the setup.

After the account and password has been setup, the next time user opens the ICMS,   when the login window appears, the user can type in the newly registered username   and password to login ICMS.

| Icon | Description |
| --- | --- |
|  | Add a user account. The default authority is with none permission. |
|  | Delete a user account. |

9-3.2 DVR CONNECTION

DVR connections can be added to or deleted from the CMS and their information can be edited. DVR’s channel names can be entered here or downloaded from the DVR by pressing ‘‘FROM DVR’’.  Select “OK” to save the information.

Note that, (1) the user name and password refers to the account setup in the DVR. To register a new account, please refer to Section 5.5. (2) Each DVR setup slot is only for an individual user. If you have more than one user connecting to the same DVR,      please add a DVR setup slot for each user.

| Icon | Description |
| --- | --- |
|  | Add a DVR for a specific user. |
|  | Delete a DVR for a specific user. |

9-3.3 GROUP SETUP

A ‘‘GROUP’’ means a set of video channels from one or many DVRs, which means, user can organize channels from different DVRs to be set in a group. This function allows you to monitor and manager channels from multiple DVRs easily and flexible.

Steps：

Add a new group and set its name and description.

Click ‘’SELECT’’ which will bring up a new window.

Check the specific channels that you’d like them to be included in the group. To include all channels of a DVR, just check the DVR.

| Icon | Description |
| --- | --- |
|  | Add a group for a specific user. |
|  | Delete a DVR for a specific user. |

Click “OK” to return to the previous window.

Select a display mode.

Drag a channel from the lower left panel into the main display to a preferred location. Or, change the channel location in the main display by mouse dragging.

You can ‘’SELECT’’ again to add other channels, but the un-saved channel locations will be lost.

Click “OK” to save the setup.

9-3.4 eMap SETUP

With eMap, the user can choose a map and place the camera channels on this map. Inthis way, it is very easy to identify where the camera is located. With eMap, the background map can be picked by the user and camera channels from multiple DVRs can be placed and dragged around onto the picture.

Steps to follow：

Click  and a path for the picture will be prompted.

Select a picture, click OK and the picture will show in the right panel.

Drag channels in the left lower corner onto the picture to any position.

To delete a channel already on the picture, right click the channel and click ‘‘REMOVE’’.

Click OK to save.

9-4 REMOTE SURVEILLANCE MANAGEMENT

After setting up the users, DVR connection and groups, you are ready to start  remote surveillance.

9-4.1 VIEW A DVR／GROUP LIST

| Icon | Description |
| --- | --- |
|  | View list of logged in DVR／Group. |

Single left click on ‘‘DVR’’ or ‘‘GROUP’’ will

expand/collapse the entire DVRs and

groups list.

On the DVR list, double left click on a

connected DVR will show its image in

the main display..

On the Group list, double left click on a

group will show live image from the

channels of the group in the main

display.

Left-clicking on a connected DVR will expand/collapse status of its all channels as below：

| Icon | Description |
| --- | --- |
|  | Video Loss |
|  | Motion Detected |
|  | Sensor Triggered |

9-4.2 VIEW EVENT LOGS

Under this page, all the events of a DVR can be expanded/collapsed in the order of Remote in/Remote out, Video Loss, Motion, Sensor, Others (Power Reset, Key Lock, Key Unlock, HD Full).

9-4.3 MAIN DISPLAY

The main display area is where the live image of DVR is shown. You can drag to change the location of screen for each channel and turn on∕off audio signal with mouse-click.

9-4.4 AUDIO CONTROL

In live mode, you can turn on/off the audio signal of CH1~CH4：

「」：Audio signal is On

「」：Audio signal is Off

Turn on∕off by clicking on the graphical icon, please note there can allow only one channel’s audio signal to be on at one time.

9-4.5 eMAP DISPLAY

In Live mode, pressing  will bring the e-MAP drag-down menu. If the channel has been set up to use e-MAP, the menu will show all the e-MAP titles that have been entitled to this channel; otherwise, “NO eMAPS” will be shown. Please check “9-3.4 eMAPSETUP” for setup information.

When you choose the eMap, the camera channel displays will be shown on the eMap.

9-4.6 PTZ CONTROL

In the main display, right click on the channel will bring up PTZ control panel as below.

| Icon | Description |
| --- | --- |
| 8 DIRECTION KEY | Rotate the PTZ |
|  | ZOOM+：Zoom-in |
|  | ZOOM-：Zoom-out |

9-5 LOCAL PC VIDEO RECORD AND INFORMATION

The video record, snapshot control and information is located at the left lower corner of the screen. Please see the chart below：

| Icon | Function | Description |
| --- | --- | --- |
|  | HDD INFO | Shows the ratio of available space∕HDD size of the C:\ drive (where CMS is installed). |
|  | VOLUME | PC volume or playback volume control bar. |
|  | RECORDING | Record live image to local PC storage. To view locally stored data, use “RECORD” under the operation bar. Also see “9-6.6 HDD PLAYBACK” for detail. |
|  | SNAPSHOT | Take snapshot to save in local PC storage. To view all the snapshot you’ve taken, please go to ”SNAPSHOT” under the operation bar. See “9-6.5 REMOTE PLAY” for detail. |

9-6 PLAYBACK VIDEO

9-6.1 REMOTE PLAY

Video images recorded on a DVR can be displayed on a remote CMS. With Remote Play function, select a DVR and a display mode on top of the screen. After the recorded segments are listed below, double click on one to show its image on the right.

| Icon | Description |
| --- | --- |
|  | Start playing. |
|  | Pause. |
|  | Fast forward. |
|  | Fast rewind. |

9-6.2 HDD PLAYBACK

You can directly play the recording data in the HDD that’s uninstalled from DVR by CMS. See the picture below, the left part of screen is recording data in list that’s separated by hour and the right part is main display. You can change the display modes and play files fast forward or rewind.

9-6.3 FILE PLAYBACK

The flash disk backup from the DVR is saved as .IRF files. You can play the recorded .IRF files by “FILE PLAY” in CMS. It allows you to change the display mode, forward or rewind the file and drag the time bar.

| Icon | Description |
| --- | --- |
|  | Start Playback. |
|  | Pause. |
|  | Stop playback. |
|  | Fast forward. |
|  | Fast rewind. |

9-6.4 EVENT PLAYBACK

Event recordings on the DVR can be played back in CMS.

Steps to follow：

- Select a DVR

- Select a display mode.

- Select a date.

- Double click an event and play back the images on the right.

Use buttons at the bottom to control the playback.

| Icon | Description |
| --- | --- |
|  | Start Playback. |
|  | Pause. |
|  | Fast forward. |
|  | Fast rewind. |

9-6.5 SNAPSHOT DATA

It can display all the snapshots you’ve taken in line in “SNAPSHOT DATA”. You can

review, delete or save as other files here.

9-6.6 RECORDING DATA

It can play all the recording files you’ve recorded in line in “RECORDING DATA”. You can play or delete them here.

Steps：

- Choose the recording time at upper left corner, it will be played on the main display.

- You can choose the display mode.

- Time bar will be shown at right lower corner, please drag the time bar to specify the    recording time you’d like to play.

APPENDIX I HARD DISK INSTALLATION

- Unscrew the screws on the cover. (2 screws on each side, and 3 in the back)

- Take off the cover. Place the HDD on the HDD rack and plug SATA connection.

- Screw up the HDD onto the HDD rack. Please screw up on both sides.

- Put back the cover and screw the cover up. Now the installation is done.

APPENDIX II TROUBLE SHOOTING

DVR Related Problem

Q.	Why the DVR cannot record any video?

A.	Make sure you have correctly setup the recording. Please check if you have setup certain things in the main menu:

(1) Go to utility -> HDD Initialization and format the HDD.

(2) Go to the record setup, and check “Schedule – Record Normal”.

(3) Go to the schedule setup, and setup a schedule. Make sure you enable this schedule and check “Schedule – Record Normal”.

Q.	I have setup the motion detection, but it still does not work.

A.	To make sure you have correctly setup the motion detection, please check if you have setup certain things in the main menu:

(1) Go to the record setup, and check “Schedule - Motion”.

(2) Go to the event setup, enter motion setup, and check “Motion Detection”.

(3) Go to the schedule setup, and setup a schedule. Make sure you enable this schedule and check “Schedule - Motion”.

Q. 	I have setup the alarm detection, but it still does not work.

A. 	To make sure you have correctly setup the motion detection, please check if you have setup certain things in the main menu:

(1) Go to the record setup, and check the “Schedule - Sensor”.

(2) Go to the event setup, enter sensor setup, and check “Sensor Detection”.

(3) Go to the schedule setup, and setup a schedule. Make sure you enable this schedule and check the “Schedule - Sensor”.

iCMS Related Problem

Q.	When I setup a DVR through DVR administration, what should I type for the ID/Password? Is it the username/password setup in the CMS, or the username/password setup in DVR?

A. 	The ID/Password is the username/password setup in DVR. Please identify the ID and Password that you use, is registered in the DVR, and has been enabled. To register this ID/Password, go to main menu -> account setup, and type in the username/password. Please check on the number to activate it.

# Text boxes

⑫   ⑪  ⑩   ⑨                ⑧       ⑦

(16) Stop (down)

This document contains preliminary information and subject to change without notice.

(17) Enter (Mode)

(15) Slow Forward (up)

(14) Fast Forward (right)

(13) Rewind (left)

(12) Play

Backup

(See Section 6.1)

Search Setup

(See Section 6.2)

Main Menu

(See Section 5.1~5.10)

Click here to setup

Quad

Display

Full Screen Display

Display

Setup

(11) Power (DC12V)

(4) Audio Out

(8) LAN

(7) Function

(5) VGA Out

(6) Camera Power

(11) Pause

(3) Audio In

The Operation of H.264Pocket

(10) Record

(2) LEDs

(3) Backup

(1) USB

(9) Menu

(8) ESC

(7) Search

(2) Video In

(1) Video Out

Playback

(See Section 4.2)

Utility Setup

Diagnostic

System Setup

PTZ & RS485 Setup

| Button Name | Description |
| --- | --- |
| 1. REC | Start/Stop recording. |
| 2. | Audio |
| 3. ◀◀ ▌▌ ■ ▶▶ | Fast forward；Pause；Stop；Fast rewind |
| 4. BK-UP | Display backup menu. |
| 5. STATUS | Display status. |
| 6. SLOW | Press this button to slow-down playback speed |
| 7. MODE |  |
| 8. 1,2…7,8,9, +10 | Select the channel to monitor in full screen from 1 to 16 |
| 9. | Switch to Quad∕9∕13∕16 channel display |
| 10. LOCK | Enable/Disable the keypad function on the front panel, the remote control and the mouse. |
| 11. PLAY | Start playing back the most recently recorded segment. |
| 12. T-SRH | Display search menu. |
| 13. | (：Up (：Down (：Left (：Right ENTER | Direction and ENTER buttons. |
| 14. MEMU | Display setup menu. |
| 15. ESC | Return to the previous mode. |
| 16. Z+∕Z- | PTZ zoom-in∕out. |
| 17. IRIS +∕- | PTZ iris-open∕close. |
| 18. F+∕- | PTZ focus-in∕out. |
| 19. OSD | Turn on∕off the screen display. |
| 20. PRESET |  |
| 21. TOUR | Activate PTZ pre-set tour. |
| 22. PTZ | Start/Stop PTZ control. |
| 23. AUTO | In AUTO mode, all available channels will be cycled through in full screen. |
| 24. FREEZE | Turn on/off screen freeze function |
| 25. PIP | Turn on picture-in-picture format. Click on the channel name can switch to other channels. |
| 26. ZOOM | Enable/Disable double screen size display. |

4. Choose an event to playback,

2. Choose a display mode

5. Play the video with these controls

3. Choose a date to playback

Regulatory

FCC Certification

This equipment has been tested and found to comply with the limits for a class A digital device, pursuant to Part 15 of the FCC rules. These limits are designed to provide reasonable protection against harmful interference when the equipment is operated in a commercial environment. This equipment generates, uses, and can radiate radio frequency energy and, if not installed and used in accordance with the instruction manual, may cause harmful interference to radio communications. Operation of this equipment in a residential area is likely to cause harmful interference in which case the user will be required to correct the interference at their own expense.

CE Mark

This product is marked with the CE symbol and indicates compliance with all applicable EEC directives.

2. Choose a display mode

(9) NTSC/PAL Switch

Record On/Off

- Choose a DVR to playback

PTZ Setup

(See Section 4.3)

Setup

Move your mouse   here to setup!

(10) Spot Monitor

The Operation of Jrviewer

(5)

(1)

(2)

1

2

3

4∕5

6∕7

8

9

10

11/12

13

14/15

16

17

18

19∕20

21∕22

23∕24

25∕26

(4)

(3)

H.264  4 Channel DVR

User Manual

(4) PIP display

Network Setup

Account Setup

Camera Setup

Schedule Setup

Event Setup

Record Setup

(6) Sequence display

(5) Zoom

Public Static IP (LAN port for Router)

Eg. IP: 61.201.78.21

Mask: 255.255.255.248

Public Static IP

Eg. IP: 61.201.78.22

Mask: 255.255.255.248

or SWITCH

Public Static IP (WAN port)

Eg. IP: 61.201.78.21

Mask: 255.255.255.248

Private Static IP

Eg. IP: 192.168.1.20

Mask: 255.255.255.0

Public Static IP (WAN port)

Eg. IP: 61.201.78.21

Mask: 255.255.255.248

Private Dynamic IP

(LAN port)

Eg. IP: 192.168.1.20

(assigned by Router)

Mask: 255.255.255.0

Dynamic IP Configuration

IP: 192.168.1.1

Mask: 255.255.255.0

Setup DDNS setting

PPPoE mode

DDNS configuration

Enable DDNS on DVR

Setup the domain name

Username: jack

Password: jack

Backup

(See Section 6.1)

Search Setup

(See Section 6.2)

Press ▲ or ▼ to move the   cursor and select either hour, minute, second etc. Press ◀ or ▶to change the values.

Pull the time bar with a mouse to select a specific time region. Press “Enter” or left  click with a mouse to playback video.

The SATA connection

The HDD rack

Plug the SATA connection

(1) Click here to start user setup (See 9-3.1)

(2) Click here to connect to DVR (See 9-3.2)

(3) Click here to arrange your cameras (See 9-3.3)

(4) Click here to add a eMap (See 9-3.4)

Click here to provide the user authority to certain actions.

Type in the user name and password for 	  each user

Each slot is only for a user.

Type in the user ID and    password to allow this user to use this DVR connection.

Type in the IP address and port number for this DVR.

- Click the group and a window will pop out.

2. Click the camera channels to be use in this group.

3. The chosen cameras will 	appear in this window. 	Drag them to the right 	and place them.

4. The cameras are arranged	Note that, for different 	number of channel 		display, you can arrange 		cameras in a different 	way.

3. The camera channel and

description will be shown on 	the picture

- Choose a map, which is stored as a jpeg file,

from the PC. The

picture will load onto the right screen

2. Drag the cameras to the

picture on the right

- Click here and the list will

collapse

2. Click here and the 	camera views will be 	shown on the screen

(4) Playback video events stored

in DVR (See 9-6.4)

(3) Playback video backup in

a flash disk (See 9-6.3)

(6) Playback video recorded by CMS, (See 9-6.6)

(1) Playback video stored in DVR 	(See 9-6.1)

(5) View snapshots (See 9-6.5)

(2) Playback video in HDD uninstalled from the DVR 	(See 9-6.2)

Choose a DVR to playback

Choose a time region to playback

Play the video with these controls

Choose a time region to playback

Uninstall the HDD in DVR and connect to the PC

Choose a display mode

Play the video with these controls

Choose a display mode

Choose a .IRF file to playback

Play the video with these controls

- Choose a video to playback

3. Play the video with these controls

The camera display

The main menu is

shown on a right click

Graphic icons to show each

camera status. (See Section 4-1.2)

Graphic icon to show network status.

Current date and time.

Playback the video stored in the DVR. (See Section 4-2)

Use PTZ function to move the camera. (See Section 4-3)

Graphic icons to show the recording status.

(See Section 4-1.2)

The Menu (See Section 4-1.2)