|  | Compact package, includes connectors for ease of installation Design for G.lite Application 100 mA DC Loop Current Capacity ★ GOLD PLATING: 50u” |
| --- | --- |
| Specifications |
| POTS Port Impedance | 600Ω |  | DC Resistance each line | 12.5Ω Max |
| Insertion Loss @1004Hz | -0.3dB Max |  | Return Loss @SRL-L | 30 dB Min |
| 200Hz~3.4KHz | +/-0.5 dB |  | @ERL | 20 dB Min |
| 3.4KHz~4.0KHz | +/-0.75 dB |  | @SRL-H | 17 dB Min |
| Insertion Loss @1004Hz / 5 Filter | -0.5 dB Max |  | Attenuation @30 KHz | -26dB Min |
| 200Hz~3.4KHz | +/-2.5 dB |  | @1MHz | -65dB Min |
| 3.4KHz~4.0KHz | +/-4.0 dB |  |  |  |
| Isolation resistance tip/ring | 10M ohm Min |  |  |  |
| Dimension Schematic Data sheet subject to change without notice |

# Text boxes

| Connector | Function | Style | Tip | Ring |
| --- | --- | --- | --- | --- |
| J1 | Modem | RJ11 | Pin3 | Pin4 |
| J2 | Line | RJ11 | Pin3 | Pin4 |
| J3 | Phone | RJ11 | Pin3 | Pin4 |

RJ11

6

1