S-SA8F-IR

Features                          Viewing picture at night

• Die casting aluminum housing, strong and durable

• Support brightness adjustment

• Support light sensor sensitivity adjustment

• IR pass panel, delicate and covert

• IP66 waterproof

• 2years warranty

Technical Specification             Drawing

LED type: 8 pieces high power 1W IR LED

Wavelength: 850nm

Beam angle: 15° to 120°

Beam distance: 100m to 15m(850nm)

Bracket: wall mount bracket

Working voltage: AC110-220V

Power consumption: ＜12W

Day/night switch: 0-50LUX adjustable

Brightness adjust: 5%-100% adjustable

Working temperatures: -20°C to 50°C

Protection level: IP66

Color: white

Panel: tempered glass + IR passing panel

Housing: aluminum die-casting housing

Net weight: 0.9kg

Gross weight: 1kg                                     Unit: mm

Model for Selection                  Product Certificate

Model        Beam angle   IR distance(850nm)

S-SA8F-15-IR       15°           1m-100m

S-SA8F-30-IR       30°           1m-70m

S-SA8F-45-IR       45°           1m-50m

S-SA8F-60-IR       60°           1m-35m

S-SA8F-90-IR       90°           1m-25m

S-SA8F-120-IR     120°           1m-15m

*Viewing distance is depending on the technical

specification of camera and lens.

# Text boxes

With IR light          Without IR light