## Key Features

- Attractive styling Design

- High Reliability Die-Cast

Aluminum Alloy Construction

- Cable Entry with IP68 Glands

- High Wear / UV Resistant

###### Rubber Seal

- Stainless Allen-head Screws for

Tampering and Rust prevention

- 3 mm Temper glass window with

High Reliability Gel

- Weatherproof to highest level IP68

- Robust Cable management bracket assembly

- Designed for Indoor/Outdoor Applications

- Easy Access for Servicing and Installation

- Fused input terminal block

- Models Available with Factory-Installed

Heater and Blower with Multiple voltage option

# Text boxes

The VISUS CITY Series comprises a stylish pressure die cast enclosure, sized to suit CCD cameras with fixed focus lenses, plus wall bracket with cable management system.

The equipment has a compact body length of 13.38 (base) and 14.76 (overall) inches (34.0 and 37.5 cm, respectively).

VISUS CITY Series is designed to provide the installer with a secure and reliable camera option.

The internal camera cavity is simply accessed by loosening 3 stainless Allen screws. Two adjustable glands (PG13.5) on the bottom of the enclosure allow for easy installation of the power and video cables.

PATENTED H1B1 ENCLOSURE AND MOUNT

TECHNICAL DATA

VISUS CITY | 2/3

| VISUS CITY Series |
| --- |
| MODEL | Basic Enclosure & Mount | Heater 12Vdc / 24Vac | Heater 100 ~ 240Vac | Blower 12Vdc | Blower 24Vac | Max. Consumption |
| VISUS CITY 124H | ◆ | ◆ |  |  |  | 30W |
| VISUS CITY 230H | ◆ |  | ◆ |  |  | 40W |
| VISUS CITY 12HB | ◆ | ◆ |  | ◆ |  | 34W |
| VISUS CITY 24HB | ◆ | ◆ |  |  | ◆ | 34W |

PRODUCT SPECIFICATION

VISUS CITY Series Enclosure

H1B1 Series Enclosure

TECHNICAL DATA

| GENERAL |  |
| --- | --- |
| Construction | Entirely made of die-cast aluminum alloy |
| Finish | RAL 9010 color of UV rays resistant powder coat |
| Environment | Totally protected against dust and any water from all directions |
| Weight |  |  |
|  | VISUS CITY 124H 5.25 lb (2.38 kg) |  |
|  | VISUS CITY 230H 5.25 lb (2.38 kg) |  |
|  | VISUS CITY 12HB 5.68 lb (2.58 kg) |  |
|  | VISUS CITY 24HB 5.68 lb (2.58 kg) |  |

| MECHANICAL |  |
| --- | --- |
| Window 4 mm thick tempered glass 82 x 68 mm ( W X H ) in viewing |
| Enclosure Length base 340 mm overall 375 mm Width 145 mm, Height 110 mm |
| Internal usable area 250 mm length 110 mm Width 70 mm Height |
| Certification Meets international IP68 standard |
| Camera mount Slot plate for adjustable camera positioning |
| Certification Meets international IP68 standard |
| Cable Entry 2 X PG 13.5 IP68 rating cable glands |

VISUS CITY Series Enclosure

VISUS CITY | 1/3

VISUS CITY | 3/3

| MECHANICAL |  |
| --- | --- |
| Bracket Robust wall mounting design , Length 330 mm Fully adjustable swivel head by 2 stainless steel allen-head screws Very good resistance to swaying Tilt angle of +40° to -150°; Pan angle of +100° to -100° Load rating: 76 lb (30kg) |
| ELECTRICAL |  |
| Heater control Below 15°±3°C automatic turning on Above 25°±3°C automatic turning off Blower control Above 35°±3°C automatic turning on Below 25°±3°C automatic turning off |
| Terminal block Fuse input ( Max. 400V ) |

VISUS CITY Series Enclosure

TECHNICAL DATA