DYNAC●L●R  D7004 DVR

Features:

- Support NTSC and PAL system

- Real time display

- Front panel operation extended from Time Lapse VCR

- Programmable recording picture rate

- Record in Quad/ Mux mode

- Swappable HDD

- User friendly video search (Date/ Time)

- Password to secure installation authorization

- System auto reboot after power interruption

- System software stored in nonvolatile memory, free from hard disk crash

Specification:

| Model Name | D7004 |
| --- | --- |
| Compression Format | Advanced M-JPEG |
| Video System | NTSC | PAL |
| Live Display Resolution | 720 X 480 | 720 X 576 |
| Live Display (pps) | 120 pps (4x30 pps) | 100 pps (4x25 pps) |
| Resolution-Recorded (per channel) | Mux | 640 X 224 | 640 X 272 |
|  | Quad | 320 X 112 | 320 X 136 |
| Recording Rate (pps) | Mux | 30 pps | 25 pps |
|  | Quad | 120 pps | 100 pps |
| Recording Mode | Manual/ Schedule/ Alarm |
| Recorded Image | Quad/ Mux |
| Video Input | BNC X 4, 1.0 Vp-p, 75 ohm |
| Video Output | BNC X 1, 1.0 Vp-p, 75 ohm |
| Fast Playback | YES |
| Alarm Input | X 4, Terminal Block |
| Alarm Out | X 1, Terminal Block |
| Power Supply | DC 12 V/ 2A |
| Dimensions | 432 (W) X 47 (H) X 270 (D) |

2003/05/07