MODEL: D7963 MUXDVR

16-CH MULTIPLEXED  DIGITAL VIDEO RECORDER

DYNACOLOR D7963 MUXDVR is a state-of-the-art 16 channel multiplexed digital video recording system, equipped with proprietary real time operating system, powerful Wavelet compression engine, duplex  multiplexer front-end, and the most popular storage device – Hard Disc Drive.

D7963 extends from the same easy-to-use user interface and functions (motion detection, alarm processing) that DynaColor’s Multiplexer provides. Digital recording with Wavelet CODEC enables D7963 more efficient recording and quality image retrieving than ever.

Packed with one mobile rack for hot swappable HDD at the “Windows” compatible data format, D7963 allows user to remove it and plug into PC for the viewing, print-out, archiving, or transmission of the video clips been stored. Video Clip can be exported to on board CDR/W for distribution of evidence. D7963 also allows users to access live and recorded video from remote site through Internet with Ethernet port connected. RS-485 communication port enables integration with other security control devices.

D7963 keeps heritage of DynaColor’s Multiplexer family with same powerful multiplexer functions, and incorporates the latest Wavelet compression technology plus a hot-swappable hard disc drive into one chassis. D7963 features not only a user friendly and cost effective digital video recording system, but also offers better image retrieve than conventional multiplexer and time lapse VCR combination.

SPECIFICATION

| MODEL NAME | D7963 |
| --- | --- |
| Compression Method | Wavelet |
| Video System | NTSC | PAL |
| Resolution - Live Video | 720 x 480 pixels | 720 x 576 pixels |
| Resolution - Recording | 720 x 240 pixels | 720 x 288 pixels |
| Recording Rate | Up to 60 PPS | Up to 50 PPS |
| Recording Device | Hot Swappable HDD |
| Recording Quality | 5 Levels selectable |
| Video Clip Export | Built-in CD-R/W (Optional) |
| Video Input | BNCx16, 1.0Vp-p, 75 ohm |
| Video Looping Through | BNCx16, 1.0Vp-p, 75 ohm |
| Main Monitor Output | BNCx1, S-VHSx1, 1.0 Vp-p, 75 ohm |
| Call Monitor Output | BNCx1, 1.0 Vp-p, 75 ohm |
| Alarm Input | x16, DSUB 37pin male, (TTL level) |
| Alarm Output | x1, DSUB 37pin male, 2.0A/24V |
| Networking | Ethernet (10 Base-T) |
| Remote Control | RS-485 DSCP |
| Playback Speed | Fast Forward/ Rewind (x1~ x8), picture by picture |
| Zoom | Yes, 2x2 |
| Power Supply | DC12V / 4A |
| Title | 12 characters |
| Alarm List | Up to 255 events |
| Dimensions (W x H x D) | D7963: 432x45x400mm D7963-C: 432x88x400mm |
| Operating Temperature | 0~40(C |

SYSTEM ARCHITECTURE

PRODUCT SELECTION GUIDE

7963- X1   H    X3    X4

| P:PAL | C: with CD-RW | L: with LAN |
| --- | --- | --- |
| N:NTSC | X: without CD-RW | X: without LAN |

Developed and Manufactured by:

DYNACOLOR, Inc.

NO.116, Jou Tz St., Neihu, Taipei 114, Taiwan, R.O.C.

Tel: 886-2-2659-8898    Fax: 886-2-2659-8868

E-mail: sales@dynacolor.com.tw

Http: www.dynacolor.com.tw

# Text boxes

KEY FEATURES

- Powerful Wavelet compression

- Proprietary real time O.S.

- Half duplex operation: Monitor Live and Playback video at the same time

- Support NTSC and PAL system

- Programmable recording picture rate (up to 60 PPS)

- Recording priority of each camera dynamically adjusted by motion detection

- Hot swappable HDD

- Data format compatible with PC

- Powerful Alarm Processor allows flexible alarm trigger and response configuration

- Programmable motion detection area and sensitivity for each camera individually

- Intelligent algorithm refreshing main monitor display dynamically

- User friendly video search

- Versatile multiple-window display format

- Password to secure installation authorization

- System auto reboot after power interruption

- System software stored in nonvolatile memory, free from hard disk crash

DYNAC(L(R

MKPB-D7963-00

16-CH MULTIPLEXED

DIGITAL VIDEO RECORDER

KEY FEATURES

- Powerful Wavelet compression

- Proprietary real time O.S.

- Support NTSC and PAL system

- Programmable recording picture rate (up to 60 PPS)

- Dynamic recording priority adjustment and display refreshing based on motion detection

- Hot swappable HDD

- Build in CDR/W for video clip export

- Data format compatible with Windows

- Powerful Alarm Processor allows flexible alarm trigger and response configuration

- Programmable motion detection area and sensitivity for each camera respectively

- User friendly video search

- Versatile multiple-window display format

- Password to secure installation authorization

- System auto reboot after power interruption

- System software stored in nonvolatile memory, free from hard disk crash

- Windows Application software available

- P/ T/ Z control available

- Remote monitoring and control through Internet or Ethernet

DYNAC(L(R

MKPB-D7963-02

##### MODEL D7963 MUXDVR

###### DYNACOLOR D7963 MUXDVR

D7963 FRONT PANEL

| CAMERA 1~16 | 8. SET |
| --- | --- |
| GOTO | 9. SEQ |
| FAST REWIND/ BEGIN | 10. MODE |
| PLAY | 11. MENU |
| PAUSE | 12. ESC |
| FAST FORWARD/ END | 13. ENTER/ ZOOM |
| 7. DIRECTION KEYS |  |

D7963 REAR PANEL

| 1. External IDE | 6.External I/O |
| --- | --- |
| 2. RS-485 Port | 7.Main Monitor(S-VHS) |
| 3. Main/ Call Monitor(BNC) | 8.Camera Looping |
| 4. LAN Port | 9.Power Jack |
| 5.Video In |  |

WINDOWS APPLICATION SOFTWARE

Note: This document is subject to change without notices.

6             7                                                  8                                           9

1           2     3     4                                                                                       5

8    9           10     11 12                13

1                     2     3    4     5    6                    7

Represented by:

Worldwide Distribution and Service Network

20030805