LOW COST

## DIGITAL MULTIPLEXER

MODEL: D72X1 SERIES

LOW COST DIGITAL MULTIPLEXER

DYNACOLOR D72X1 series digital multiplexer utilizes state-of-the-art technology to provide high video quality images and the best cost-effective solution for security surveillance application. Intelligent embedded software delivers sophisticated functions while keeping the user interface simple and friendly.

Duplex operation allows video recording while viewing live video (from camera) or video playback (from VCR). Outstanding picture quality is ensured with the latest hardware technology. RS-485 communication port enables smooth integration with other security control devices.

Eight segment gain control available for each camera input individually camera signal level difference is compensated to achieve concordant display on the monitor.

DYNACOLOR D72X1 Series Low Cost Digital Multiplexer

SPECIFICATION

| Model | D7241 | D7291 | D7261 |
| --- | --- | --- | --- |
| Maximum inputs | 4 | 9 | 16 |
| No. of alarm inputs | 4 | 9 | 16 |
| Display format | 1, 4 | 1, 4, 9 | 1, 4, 9, 16 |
| System operation | Duplex |
| Active resolution | NTSC: 720 x 480 |
|  | PAL: 720 x 576 |
| BW / Color | 256 gray levels / 16 M color (Y: 8, U: 8, V: 8) 4: 2: 2 |
| VCR Input | BNC and S-VHS |
| VCR Output | BNC and S-VHS |
| Main monitor output | BNC and S-VHS |
| Call monitor output | BNC |
| Gain control | 8 Segment/per camera (Range: 70%~140%) |
| Camera looping | Yes (75Ω terminator programmable by software) |
| No. of alarm outputs | 2 (N.O., N.C.) 2.0A/24V |
| Motion Detection | Yes |
| Video loss indication | Yes |
| Motion detection area | 192(16 x 12) dots per camera |
| Picture freeze | Yes |
| Recording mode | Synchronous (Time Lapse): By VCR trigger |
|  | Asynchronous (programmable): 2, … , 960(NTSC/EIA) 3, … , 960(PAL/CCIR) |
| Recording rate | 30 frames/sec |
| Playback Date/Time display | Yes (programmable) |
| Sequence page | Full | Full, Quad | Full, Quad, 3 x 3 |
| Key lock function | Yes |
| Camera title size | 12 characters per camera (programmable) |
| Alarm history log | 255 events |
| Remote control | RS-485 |
| Color bar generator | Yes |
| Input voltage range | 12V ±10% |
| MAX Power | 14W |
| Temperature | 0℃~40℃ |
| Humidity | 0~90R.H |
| Weight | 3.7 kg |
| Dimension (mm) | 432(L) x 270(W) x 44(H) |

**This document is subject to change without notices.

OPTIONAL CONTROL KEYBOARDS

( Model D731X for Multiplexer, and Dome Camera control

Developed and Manufactured by:

DYNAC(L(R

彩富電子股份有限公司

114 台北市內湖區洲子街116號

No. 116, Jou Tz St., Neihu, Taipei 114, Taiwan, R. O. C.

Phone: 886-2-2659-8898     Fax: 886-2-2659-8868

E-mail: sales@dynacolor.com.tw

http://www.dynacolor.com.tw

# Text boxes

KEY FEATURES

- Duplex operation

- Color (NTSC/PAL) and Mono (EIA/CCIR) models available

- 720 x 576 pixel display with 256 gray levels and 16 million colors

- Compatible with color and B/W video cameras

- Recording rate: 30 frames per second

- Compatible with standard BNC and S-video VCR connectors

- Support double/triple density VCRs

- Gain control for each camera

- Invisible & install camera set up for each camera

- Camera auto detect

- Motion detect

- Three sequence mode

- Nonvolatile memory protects system setup from power loss

- Alarm history log up to 255 records of event

- User friendly OSD menu (On Screen Display)

- Build in color bar generator for monitor calibration

- Optional remote control keyboards available

DYNAC(L(R

MKPB-72X1-03

### FRONT PANEL

- CAMERAS SELECT KEY

- FUNCTION KEY

- DIRECTION KEY

### REAR PANEL

- RS-485

- MONITOR (CALL / MAIN) OUTPUT

- VCR INPUT / OUTPUT

- VIDEO INPUT / OUTPUT

- ALARM INPUT / OUTPUT

- POWER INPUT

#### PRODUCT SELECTION

##### D72X1-R        X

*Must specify on order placement*

4: 4 channel

9: 9 channel

6: 16 channel

1                           2

P: PAL / CCIR

N: NTSC / EIA

Represented by:

Worldwide Distribution and Service Network

MODEL D72X1 SERIES

3

1     2   3                4

5                                          6