# Text boxes

### PRODUCT FEATURES

Standard Features (All Models)

- 5” Compact, Low Profile Color Dome Camera

- 360° Continuous Pan Rotation

- Continuous Auto Focus

- Variable Speed 1° ~ 375°

- Auto Turn Around Function

Digital Flip (23x,25x only)

- 128 Presets

- Home Position

Privacy Masking (23x,25x only)

- Pan/Tilt Speed Proportional to Zoom Ratio

- 25X Optical Zoom, 12X Electronic Zoom (Optional)

- Minimum illumination: 0.01 Lux (Optional)

- Advanced DSP Camera

˙Auto White Balance

˙Backlight Compensation

˙Auto Iris Control

˙Electronic Shutter

- Remote Control via RS-485

- Built in 4 Alarm Inputs

- On Screen Display for Camera Control

- 12VDC/ 24VAC Model Available

- 24VAC Line Lock

- Twist Lock Release from Base for Easy Installation and Servicing

Outdoor Housing Features

- Environmentally Sealed

- Sun Shield

D7913

Advanced Video Recorder

D7963

## MUX DVR

Features

- Wavelet Codec + Proprietary real time O.S.

- Dynamic recording priority adjustment and display refreshing based on motion detection

- Hot swappable HDD

- Data format compatible with Windows

- Programmable motion detection area and sensitivity for each camera respectively

- System auto reboot after power interruption

- Windows Application software available

HOUSING for OUTDOOR

- Easy Installation

- Built in Fan

- Optical Clear Dome Cover

- Different Pendant Available

- Environmentally Sealed and Weatherized for use in Temperatures to 50°C

- Power Input Available Type:

“AC 24V in” to AC24V Dome

“AC 110V in” to DC12V Dome

“AC 220V in” to DC12V Dome

- Heater is Selectable

- Sun Shield

## HOUSING for INDOOR

- Easy Installation

- Built in Fan

- Optical Clear Dome Cover

- Different Pendant Available

- Environmentally Sealed and Weatherized for use in Temperatures to 50°C

- Power Input Available Type:

“AC  24V in” to AC24V Dome

“AC 110V in” to DC12V Dome

“AC 220V in” to DC12V Dome

- Heater is Selectable

- Heater is Selectable

( HOUSING for OUTDOOR

###### GOOSENECK TUBE

- MATERIAL: IRON TUBE

- WEIGHT: 2.1 Kg

###### GOOSENECK PENDANT

- MATERIAL: ALUMINUM

- WEIGHT: 1.8 Kg

###### CORNER PLATE

- MATERIAL: SPCC Painted Black

- WEIGHT: 1.9 Kg

###### STRAIGHT TUBE 25 cm/50 cm

- MATERIAL: IRON TUBE

- WEIGHT: 1.2 Kg

( PLACEMENT EXAMPLE

##### GENERAL FEATURES

| Environment | Indoor / Outdoor |
| --- | --- |
| Controller I / F | RS-485 |
| Operating Temperature | 0°~40°C |
| Power Source | 24VAC or 12VDC |
| Power Consumption | 14.04W |
| Dimensions | Ø130x200mm |
| Weight | 1.5kg |

##### ROTARY BODY FEATURES

|  | D7722B-□□□□ | D7722C-□□□□ |
| --- | --- | --- |
| Pan Travel | 360°endless |
| Tilt Travel | D7722 □ -R | D7722□ -I | -10°~99° |
|  | D7722 □ -J | D7722 □ -S | -99°~99° |
| Manual Speed | 1°-150°/s | 1°-150°/s |
| Preset Speed | PAN | 1°-375°/s (High Res*) | 1°-375°/s (High Res*) |
|  | TILT | 6°-360°/s (Standard Res*) | 1°-375°/s (High Res*) |

*Standard: 768 steps/circle  High Resolution: 1600 steps/circle

##### CONTROL FEATURES

|  | D7722 □ |
| --- | --- |
|  | R □□□ | J□□□ | S□□□ |
| D&P protocol | Yes | Yes | Yes |
| Presets | 128 | 128 | 128 |
| Preset Accuracy | 0.50° | 0.50° | 0.50° |
| Patterns | 1 | 1 | 1 |
| Sequence | 4 | 4 | 4 |
| Auto-Pan | 1 | 1 | 1 |
| Privacy Mask | x | 2 | 24 |
| Proportional Pan & Tilt with zoom | Yes | Yes | Yes |
| Zone Title | Yes | Yes | Yes |
| Home Function | Yes | Yes | Yes |
| P/T/Z Auto-Restoring | Yes | Yes | Yes |
| Auto-Turn Around | Yes | Yes | Yes |
| Digital Flip | x | Yes | Yes |
| DSS | x | Yes | Yes |
| IR | x | Yes | Yes |
| WDR | x | Yes | x |
| Motion Detection | x | x | Yes |

###### CAMERA FEATURES

|  | D7722□ -R | D7722 □ -J | D7722 □ -S |
| --- | --- | --- | --- |
| Total Pixels | NTSC: 811(H)x508(V) PAL: 795(H)x596(V) | NTSC: 758(H)x504(V) PAL: 758(H)x592(V) |  |
| Effective Pixels | NTSC: 768(H)x494(V) PAL: 752(H)x582(V) | NTSC: 724(H)x494(V) PAL: 724(H)x582(V) | NTSC: 680k pixels PAL: 800k pixels |
| Sensor Type | 1/4” CCD | 1/6” CCD |
| Scanning System | PAL, NTSC |
| Synchronization | Internal / Line Lock |
| Video Output | 1.0Vpp / 75Ω, BNC |
| Horizontal Resolution | NTSC: 470TVL PAL: 460TVL | NTSC: 470TVL PAL: 470TVL | NTSC: 470TVL PAL: 460TVL |
| S/N Ratio | 50dB | 50dB | 49dB |
| Minimum Illumination | 1 lux | 0.01 lux 0 lux (IR illuminator) | 0.01 lux 0 lux (IR illuminator) |
| Focal Length | 4~88 mm | 3.6~82.8 mm | 2.4~60.0 mm |
| Zoom Ratio | 22X optical zoom | 23X optical zoom | 25X optical zoom |
| Digital Zoom | X1~X12 variable | X1~X10 | X1~X12 |
| Zoom Speed | 3.9 sec / 6.3 sec | 2.9 sec~5.8 sec | 2.3 sec~4.8 sec |
| Focus Mode | Auto / Manual |
| White Balance | Auto / Manual |
| Iris Control | Auto / Manual |
| Electronic Shutter | 1/60~1/30k sec. (NTSC) 1/50~1/30k sec. (PAL) | 1/2~1/30k sec. (NTSC) 1/1.5~1/30k sec. (PAL) | 1/4~1/10k sec. (NTSC) 1/3~1/10k sec. (PAL |
| AGC Control | Auto / Manual |
| BLC | On / Off |

##### DIMENSION

Represented by:

Worldwide Distribution and Service Network

Developed and Manufactured by:

DYNACOLOR, Inc.

彩富電子股份有限公司

114台北市內湖區114洲子街116號

No. 116, Jou Tz St., Neihu, Taipei 114, Taiwan, R.O.C.

Tel: 886-2-2659-8898      Fax: 886-2-2659-8868

E-mail: sales@dynacolor.com.tw

Http://www.dynacolor.com.tw

MODEL D7722

I   STANDARD SECURITY SYSTEM ARCHITECTURE   I

I   HOUSING for INDOOR/OUTDOOR SPECIFICATION   I

I   PENDANT ACCESSORIES   I

##### HOUSING SELECTION

D   7  7  H  0  0-V  T   0   0

##### PENDANT SELECTION

D  7  7  H  0  3 – B           V

I   PRELIMINARY  SPECIFICATION   I

D7312

Basic Control Keyboard

D7313

CCTV Control Keyboard

Features

- Dome/Multiplexer Can be Controlled by One Keyboard

- Friendly User Interface by LCD Display

- RS-485 Control Interface

- F/W Can be Upgraded through RS-232 Port

- Max. 255 CCTV Devices Can be Controlled (only on D7313)

- Built-in Real Time Clock Generator (only on D7313)

- Support System Clock Calibration (only on D7313)

Power

Heater

Color Of

Domed Cover

Color

Application

Type

( 0: Outdoor

( 1: Indoor

( V: White

( T: Transparent ( B: Blue

( 0: 48W

( 1: No

( 0: “AC 24V in” to

AC 24V Dome

( 1: “AC110V in” to

DC 12V Dome ( 2: “AC220V in” to

DC 12V Dome

Pendant Type

Color of Pendant

( B: Gooseneck Tude

( C: Gooseneck Pendant

( P: Corner Plate

( 1: 25cm Straight Tube

( 2: 50cm Straight Tube

( V: White

HIGH SPEED DOME 
CAMERA SERIES

# DYNAC(L(R

MKPB-7722-03

MODEL: D7722 SERIES

HIGH SPEED DOME CAMERA

D7722 is a subcompact 5” dome camera system designed for superb performance and durability. Its pristine housing looks good in any security and surveillance installation.

D7722 standard model contains new generation advanced DSP color camera, with up to 25X optical zoom and 12X digital magnifier, delivers the power of a 300X zoom to ensure that the finest details are captured. Continuous auto focus, back light compensation and auto iris control are some of the salient features incorporated to fit your needs.

High speed pan and tile, 360° endless rotation and Auto Turn Around function allows D7722 to be installed in the most demanding applications. RS-485 communication channel is available for remote control purposes, 128 preset points can be programmed for precise location of target areas, you can also define multiple sequence routes for the camera to operate automatically.

Auto Turn Around function allows the dome to rotate 180° and reposition its direction for continuous tracking of any subject that passes directly beneath the dome. Digital Flip function allows the dome flip its image for continuous tracking of any subject that passes directly beneath the dome. It is ultra fast than traditional “Auto-Flip” function. DSS and removable IR cut filter features enhance its image capture capability under very low lux environments. Wide dynamic range feature allows D7722 to deliver a clear image even the field of view contains a bright brilliantly portion and a dark portion.

Dependability and ultra high reliability are key factors in the D7722 design cycle. Every D7722 is assembled with meticulous care and thorough testing at our ISO9001 compliant factory. High performance, reliability and reasonable price, D7722 is an ideal solution to your tough surveillance requirement.

Design and Specifications are subject to change without notice. (Rev. 01.10)

##### PRODUCT SELECTION

*Standard Resolution: 768 steps/circle  High Resolution:1600 steps/circle