Digital Video Recorder

User manual

00-37913-DEA2

V1.2

Precautions

- All the safety and operation instructions should be read before the DVR is operated.

- All the safety and operation instructions should be retained for future reference.

- Comply with operating instruction and notice warning information.

- Do not use strong or abrasive detergents when cleaning the DVR.

- There are no user-serviceable parts inside. Contact qualified service personnel for maintenance.

- Do not expose the DVR to water or moisture and do not try to operate it in wet areas. Well-chosen cover is needed when you put the DVR in outdoor areas.

- Make sure that two ends of the power port are plugged.

- Do not drop metallic parts through slots or slop the DVR with any liquid.

- Do not attempt to disassemble the DVR.

- Contact qualified service personnel if the following situation happens:

- The power-supply cord or plug is damaged.

- The DVR has been exposed to rain or water.

- The DVR does not operate normally by following the operating instructions.

- The DVR falls to the ground or its cover is damaged.

- When replacement parts are required, make sure that the service technician has used replacement parts specified by original seller or that these parts have the same characteristics as the original ones. Unauthorized substitutions may result in fire, electric shock, or other hazards.

- Use only with a mounting accessory recommended by original seller.

- Never push objects of any kind into this DVR through openings as they may touch dangerous voltage points or short cut parts that could result in a fire or electric shock.

- Certify operating safety by qualified installer.

- If an outside cable system is connected to the DVR, be sure the cable system is grounded so as to provide some protection agains5t voltage surges and built-in static charges.

- All normal precautions to avoid component damage due to electrostatic discharge should be taken during installation and operation.

- To prevent electric shock, do not remove screws or covers.

CONTENT

1. Features	3

2. MUXDVR/ MUXDVR-C Application	3

3. Quick Installation Guide	4

4. Front Panel	5

4.1 Button on the Front Panel	5

5. Menu Tree	7

6. OSD Menu Setup	8

6.1 Event List	8

6.2 Date Time	8

6.2.1 Date/ Time	8

6.2.2 Date/ Time Display	8

6.3 Alarm	8

6.3.1 Alarm REC Quality	8

6.3.2 Alarm Frame Rate	9

6.3.3 Alarm REC Duration (MIN)	9

6.4 Schedule	9

6.4.1 REC Day Start/ REC Stop Time	9

6.4.2 Day REC FPS/ Night REC FPS	9

6.4.3 DAY REC Quality/ Night REC Quality	9

6.5. System	10

6.5.1 Video	10

6.5.2 Connect to MUX	10

6.5.3 Alarm IN	10

6.5.4 Circular REC	10

6.5.5 Format	11

6.5.6 Change Password	11

6.5.7 Load Default	11

6.6 CDRW Copy (for D7913-C only)	11

7. Windows Application Software	11

7.1 Connect the USB Mobile Rack to PC	11

7.2 Download the Software	12

7.3 Function Buttons	13

8. Connectors	14

9. Specification	15

Appendix : Supported H.D.D.	16

# 1. Features

- Powerful Wavelet compression

- Proprietary real time O.S.

- Simplex operation

- Support NTSC and PAL system

- Front panel operation extended from Time Lapse VCR

- Programmable recording picture rate (up to 30 fps/ NTSC and 25 fps/ PAL)

- Hot swappable HDD

- Data format compatible with Windows

- User friendly recorded video search

- Password to secure installation authorization

- System auto reboot after power interruption

- Auto re-cycle recording

- Alarm alerts while video recording approaches full capacity of HDD

- Watch-Dog-Timer to cope with unexpected power spike

- Built in CD-R/W for video clip export

- System software stored in nonvolatile memory, free from hard disk crash

# 2. MUXDVR/ MUXDVR-C Application

MUXDVR/ MUXDVR-C are a state-of-the-art 1 channel digital video recording system, equipped with proprietary real time operating system, powerful Wavelet compression engine and the most popular storage device – Hard Disc Drive. As a time lapse VCR replacement, MUXDVR/ MUXDVR-C are compatible with most of the multiplexers in the market.

# 3. Quick Installation Guide

The MUXDVR/ MUXDVR-C are equipped with a mobile rack; the HDD is hot-swappable. You can exchange the HDD when the HDD is full. The following figures illustrate how to install HDD into the removable cartridge.

Step1: Pull the active-handle outwards and unlock with the miniature key provided.

Step2: Pull the handle outwards till the carrier body is out of the cartridge.

Step3: Push the release latch to slide the top cover backwards and remove it.

Step4: Insert the DC power cable and IDE cable on the HDD. Make sure the HDD is set to “Master”.

Step5: Position the HDD into carrier body and slide the top cover back to secure. Secure the HDD using the screws provided.

Step6: Slide the carrier body back in the cartridge frame and lock it with the key provided. Then push the active-handle inwards.

# 4. Front Panel

The MUXDVR/ MUXDVR-C front panel controls enable you to perform preset and programmable functions. The figures below show the buttons available on the front panels.

Pause/ Right

GOTO/ Up    Fast Rewind/ Down

Play/ Left            Fast Forward MUXDVR

HDD R/W LED    HDD Power LED                                                                   MENU            REC LED

ESC    Power LED

MUXDVR-C

CD-RW Driver

**MUXDVR/ MUXDVR-C start detecting the camera and recording automatically after power is on.

## 4.1 Button on the Front Panel

The following are the introductions of MUXDVR/ MUXDVR-C front panel buttons. Each button is described by name and function.

HDD R/ W LED

The orange LED will be lit when MUXDVR/ MUXDVR-C are recording or playing the recorded video.

HDD Power LED

If you insert a HDD exactly, the green LED will be lit once you lock the carrier body with the attached key.

Power LED

The green LED will be lit when power on.

REC LED

The red LED will be lit when recording.

Menu/ Enter

1. Press this button to toggle the Main Menu display on/ off.

2. In OSD menu, this button is used to “enter” the sub-menu, or to confirm (execute) command.

ESC

In OSD mode, press this button to go to the previous OSD menu page.

Goto/ Up

1. Press this button to enter GoTo menu.

2. In OSD mode, this button is used as an “up” control.

REW/ Down

1. In playback mode, press this button to play the recorded video in backward direction. Press it repeatedly to choose from different rewind speed: x2, x4 and x8.

2. In OSD mode, this button is used as a “down” control.

Play-Stop/ Left

1. In playback mode, press this button to stop playing and switch to Live mode.

2. In OSD mode, this button is used as a “left” control.

Pause/ Right

1. In playback mode, press this button pause playback video or to freeze live video.

2. In OSD mode, this button is used as a “right” control.

FF

In playback mode, press this button to play the recorded video in forward direction. Press it repeatedly to choose from different speed: x2, x4 and x8.

# 5. Menu Tree

# 6. OSD Menu Setup

The OSD menu is composed in hierarchy architecture; it allows users to configure MUXDVR/ MUXDVR-C according to the application environment. To enter this OSD menu, press the MENU button of the front panel, then the OSD menu will appear with a highlight cursor over the first item. The cursor can be moved by the up and down buttons. The first four items of the menu can be entered only when the digital video recorder is recording. If you want to exit the OSD menu, you may either 1)select the last item “EXIT” and then press ENTER button; or 2)press ESC button of the front panel directly.

## 6.1 Event List

This sub-menu allows you to view the event-recorded videos. You can use the Direction buttons to select event, and press Enter button to play the event-recorded video.

## 6.2 Date Time

This menu allows you to set the current date/ time.

### 6.2.1 Date/ Time

The two items allow you to set the system current date and time. Use the right/ left Direction buttons to enter the date and time.

### 6.2.2 Date/ Time Display

This item allows you to enable or disable the date/ time OSD display.

## 6.3 Alarm

This sub-menu allows you to set up all the parameters related to alarm recording, ex. REC Quality, Frame Rate…

### 6.3.1 Alarm REC Quality

Alarm record starts when an alarm input is triggered through the I/O terminal on the rear panel. This item allows you to setup the video quality of alarm record. You can choose from: Super, High, Normal and Low.

### 6.3.2 Alarm Frame Rate

This item allows you to setup the alarm frame rate. You can choose the alarm frame rate from 30, 15, 10, 7.5, 6.5, 3, 2.5, 2, 1.5, 1, 0.5 and 0.25 for NTSC; and 25,12.5, 6.25, 5, 3.125, 2.5, 1.25, 1, 0.5 and 0.25 for PAL.

### 6.3.3 Alarm REC Duration (MIN)

This item determines how long time the DVR remains in the alarm state. You can choose the duration between 1 and 6 minutes.

## 6.4 Schedule

This menu allows you to setup the recording schedules. MUXDVR/ MUXDVR-C offer two schedules (daytime and nighttime) for you to set up according to different conditions.

Once you change parameters in this menu, the total record time will be changed as well. Below table is offered for you to refer to (the frame rate is set to 30 fps/ NTSC or 25 fps/ PAL).

| HDD Size | Total Record Time (Hour) |
| --- | --- |
|  | Quality: Super | Quality: High | Quality: Normal | Quality: Low |
| 40 GB | 7 | 9 | 12 | 15 |
| 80 GB | 14 | 18 | 24 | 30 |
| 120 GB | 21 | 27 | 36 | 45 |
| 160 GB | 28 | 36 | 48 | 60 |

### 6.4.1 REC Day Start/ REC Stop Time

These two items allow you to setup the day start/ stop time. You can use the Direction buttons to enter the desired start/ stop time.

### 6.4.2 Day REC FPS/ Night REC FPS

These two items allow you to setup the day and night record FPS (Frame Per Second) individually. You can choose from 30, 15, 10, 7.5, 6.5, 3, 2.5, 2, 1.5, 1, 0.5 and 0.25 for NTSC; and 25,12.5, 6.25, 5, 3.125, 2.5, 1.25, 1, 0.5 and 0.25 for PAL.

### 6.4.3 DAY REC Quality/ Night REC Quality

These two items allow you to setup the video quality of day and night record individually. You can choose the quality from: Super, High, Normal and Low.

## 6.5. System

This sub-menu allows engineers or installers to make advanced settings.

You cannot enter the last item while the DVR is recording; if you want to load default settings, you have to stop recording.

### 6.5.1 Video

This sub-menu allows you to adjust the video parameters including BRIGHTNESS, CONTRAST, SATURATION and HUE.

If you want to connect MUXDVR/ MUXDVR-C with a multiplexer (select “YES” for next item “CONNECT TO MUX”), then you cannot adjust these video-related settings; instead, you have to adjust those settings on the cascaded multiplexer.

Reset

This item allows you to set all changed settings to default. Move to this item and press Enter to return the default settings.

Termination

This item allows you to enable/ disable the terminal resistor.

### 6.5.2 Connect to MUX

This item allows you to connect MUXDVR/ MUXDVR-C to a multiplexer. If you want to connect to a multiplexer, you should set “YES”. MUXDVR/ MUXDVR-C are compatible with most of the multiplexers in current market.

### 6.5.3 Alarm IN

This item allows you to select N.O. (Normal Open) and N.C. (Normal Close) type for alarm relay output.

### 6.5.4 Circular REC

If you select “ON”, the recording will be continuously; the old data in HDD will be overwritten. If you select “OFF”, the recording will be stopped when the HDD is full.

### 6.5.5 Format

This sub-menu allows you to format the Hard Disk. If you want to format the HDD then you should choose the first item (FORMAT HDD    YES) and press the Enter button. If you want to keep the data in HDD, then you should select the second item (FORMAT HDD    NO) and press the Enter button to leave. This arrangement is to avoid user clearing the list by mistake

### 6.5.6 Change Password

This item allows you to change the default password (default password: 0000) to a private one. “9667” is a permanent password pervaded in case that you forgot the password you had set.

### 6.5.7 Load Default

This item allows you to reload default setting of DVR.

## 6.6 CDRW Copy (for D7913-C only)

This item allows you to backup recorded video to the CD-RW drive. Before you perform a backup, you must insert a CD or CD-RW disk into the CD-RW drive first, and then go to the sub-menu to enter the start time and end time of the wanted period. After the start time and stop time have entered, you must press Enter on “COPY” to start copying the video.

# 7. Windows Application Software

The file format of MUXDVR/ MUXDVR-C is compatible with Windows O.S; you can process recorded video data under Windows 98, 2000 and XP systems. The application software allows you to playback, printout, export JPEG file or clip a segment of video.

## 7.1 Connect the USB Mobile Rack to PC

Move out the HDD Cartridge form MUXDVR/ MUXDVR-C and insert it to a “USB Mobile Rack”, then connect the “USB Mobile Rack” and PC with a USB Cable.

## 7.2 Download the Software

To process recorded video on your computer, you need to download DVR Windows application software first. After “dvrwinap.exe” has been installed, you can now connect the swappable HDD to your computer and process the recorded video.

## 7.3 Function Buttons

1. Open File

Press this button to search and open recorded video file.

2. Print Out

Press this button to print out single picture.

3. Save Image

Press this button for saving current image (JPEG) on your P.C.

4. Display Mode

Press these buttons to choose display mode (4, 9 and 16 windows).

5. Set

Press this button to start setting windows. Use the Mouse to move the cursor to certain window, and then press a Channel button for assigning the camera to this window. The cursor will move to next window automatically.

6. Channel 1~16

Press one of these buttons to view the channel full screen.

7. Video Clipping

Press this button to clip a small period of video for transferring more easily. Press “Video Clipping” to start clipping and Press again for stop.

8. Go to Begin

Press this button to go to the first image of the recorded video.

9. Fast Rewind

Press this button to play the recorded video in reverse direction. Press this button repeatedly to change the playback speed: x1, x4, x8, x16, x32 and x64.

10. Rewind Playing

Press this button to rewind playing the recorded video at normal speed.

11. Fast Rewind

Press this button to play the recorded video in reverse direction. Press this button repeatedly to change the playback speed: x1, x4, x8, x16, x32 and x64.

12. Playback

Press this button to play the recorded video, and press it again to pause.

13. Fast Forward

Press this button to play the recorded video in forward direction. Press this button repeatedly to change the playback speed: x1, x4, x8, x16, x32, and x64.

14. Stop

Press this button to stop playing the recorded video.

15. Fast Forward

Press this button to play the recorded video in forward direction. Press this button repeatedly to change the playback speed: x1, x4, x8, x16, x32, and x64.

16. Go to End

In playback mode, press this button to go to the end image of the opened file.

17. GOTO

In playback mode, press this button for searching the recorded video of certain date and time.

# 8. Connectors

Rear Panel

| 1 | I/O Terminal |
| --- | --- |
| 2 | Video In (BNC) |
| 3 | Video Out (BNC) |
| 4 | Power Jack |

External I/O Port

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Pin No. | Definition |
| --- | --- |
| 1 | Alarm In |
| 2 | GND |
| 3 | Alarm N.C. |
| 4 | Alarm COM |
| 5 | Alarm N.O. |
| 6 | Reset Alarm |
| 7 | Trigger Out |
| 8 | RS485 D＋ |
| 9 | RS485 D－ |
| 10 | Reserved |
| 11 | GND |
| 12 | Reserved |
| 13 | Reserved |
| 14 | Reserved |

# 9. Specification

| Model Name | MUXDVR/ MUXDVR-C |
| --- | --- |
| Compression Engine | Wavelet |
| Operation | Simplex |
| Video System | NTSC | PAL |
| Resolution – Life Video | 720 x 480 pixels | 720 x 576 pixels |
| Resolution – Recorded | 720 x 480 pixels | 720 x 576 pixels |
| Recording Rate | Up to 30 Frame Per Second | Up to 25 Frame Per Second |
| Recording Device | Hot Swappable HDD |
| Recording Mode | Schedule / Alarm |
| Recording Quality | Supper / High / Normal / Low |
| Video Input | BNCx1, 1.0Vp-p, 75 ohm |
| Video Output | BNCx1, 1.0Vp-p, 75 ohm |
| Alarm Input | Terminal x1 (TTL level) |
| Alarm Output | Terminal x1, 2.0A/24V |
| Playback Speed | Fast Forward/ Reverse (x1, x2, x4 and x8), picture by picture |
| Power Supply | DC12V / 4A |
| Search by Date/Time | Yes |
| Search by Alarm | Yes |
| Alarm List | Up to 40 events |
| Dimensions | 432x44x270mm (W x H x D) |
| Operating Temperature | 0~40(C |

# Appendix : Supported H.D.D.

The supported H.D.Ds are listed as below:

| Brand | Capacity | Rotation Speed | Part Number |
| --- | --- | --- | --- |
| Maxtor | 40GB | 5400 RPM | 4D040k2 |
| Maxtor | 80GB | 5400 RPM | 4D080H4 |
| Maxtor | 80GB | 7200 RPM | D740X-6L |
| Maxtor | 120GB | 5400 RPM | 4G120J6 |
| Maxtor | 160GB | 5400 RPM | 4G160J8 |
| Maxtor | 200GB | 5400 RPM | 4G200J8 |
| SAMSUNG | 40GB | 5400RPM | SV4002H |
| Seagate | 40GB | 7200RPM | ST340021A |
| Seagate | 60GB | 7200RPM | ST360021A |
| IBM | 61.5GB | 7200RPM | IC35L060AV |
| IBM | 76.8GB | 7200RPM | DTLA30707S |
| IBM | 82.3GB | 7200RPM | IC35L080AV |
| IBM | 123.5GB | 7200RPM | IC35L120AV |
| IBM | 185GB | 7200RPM | IC35L180AV |
| Western Digital | 80GB | 7200RPM | WD800JB |
| Western Digital | 40GB | 5400RPM | WD400EB |
| Western Digital | 60GB | 5400RPM | WD600AB |
| Western Digital | 80GB | 5400RPM | WD800AB |
| Western Digital | 120GB | 5400RPM | WD1200AB |
| Western Digital | 200GB | 7200RPM | WD2000JB |

Notice : MUXDVR/ MUXDVR-C cannot support Seagate 80GB HDD (P/N 9T6006-003 firmware 3.19).

# Text boxes

**The first four items can be entered only when D7913/ D7913-C are in playback mode

FORMAT           1-5-5

FORMAT HDD                 NO

FORMAT HDD                 YES

EXIT

MENU:ENTER   ESC:RETURN

((: SELECT     ((: EDIT

1                                                                           2     3                                                                   4

FORMAT           1-5-5

FORMAT HDD      NO

FORMAT HDD      YES

EXIT

MENU: ENTER   ESC: RETURN

((: SELECT      ((: EDIT

EVENT LIST        1-1

MENU: ENTER

ESC: RETURN   ((: SELECT

1

2

3

4

CDRW BACKUP       1-6-6

BEGIN

2003/04/14   21:54

END

2003/04/16   09:45

COPY

MENU: ENTER    ESC:RETURN

((: SELECT      ((: EDIT

EVENT LIST         1-1

NO       DATE    /    TIME

1     2002/10/02     18:00:00

2     2002/10/03     00:20:01

3     2002/10/03     12:05:31

MENU: ENTER   ESC: RETURN

((: SELECT     ((: PAGE SELECT

PLEASE ENTER PASSWORD

X X X X

MENU: ENTER   ESC: RETURN

((: SELECT    ((: EDIT

SCHEDULE           1-4

START    STOP

DAY       08:00  –    20:00

FPS     QUALITY

30        SUPER

NIGHT     FPS     QUALITY

30        SUPER

ESC: RETURN

((: SELECT   ((: EDIT

ALARM              1-3

REC QUALITY                HIGH

Frame RATE                     30

REC DURATION <MIN>                1

EXIT

ESC: RETURN

((: SELECT    ((: EDIT

SYSTEM           1-5

VIDEO>

CONNECT TO MUX             YES

ALARM IN		             N.O.

CIRCULAR REC                 ON

FORMAT>

CHANGE PASSWORD>

LOAD DEFAULT

EXIT

MENU: ENTER   ESC:RETURN

((: SELECT     ((: EDIT

SYSTEM            1-5

VIDEO>

CONNECT TO MUX                 NO

ALARM IN		              N.O.

CIRCULAR REC                    OFF

FORMAT>

CHANGE PASSWORD>

LOAD DEFAULT

EXIT

MENU: ENTER   ESC:RETURN

((: SELECT     ((: EDIT

DATE TIME          1-2

DATE:  YYYY / MM / DD

TIME:   HH : MM : SS

DATE/TIME display            ON

EXIT

ESC: RETURN

((: SELECT      ((: EDIT

CHANGE PASSWORD    1-5-6

ENTER PASSWORD AGAIN

_ _ _ _

MENU: ENTER   ESC:RETURN

((: SELECT     ((: EDIT

MAIN MENU            1

EVENT LIST >

DATE TIME >

ALARM >

SCHEDULE >

SYSTEM >

CDRW COPY

EXIT

MENU: ENTER    ESC:RETURN

((: SELECT       ((: EDIT

MAIN MENU        1

EVENT LIST>

DATE TIME>

ALARM>

SCHEDULE>

SYSTEM>

CDRW COPY>

EXIT

MENU: ENTER    ESC: RETURN

((: SELECT      ((: EDIT

CHANGE PASSWORD     1-5-6

PLEASE ENTER PASSWORD

X X X X

MENU: ENTER    ESC:RETURN

((: SELECT      ((: EDIT

SCHEDULE         1-4

START    STOP

DAY      00:00  -   08:00

FPS    QUALITY

30      SUPER

NIGHT     FPS    QUALITY

15      HIGH

EXIT

ESC: RETURN

((: SELECT   ((: EDIT

DATE TIME          1-2

DATE: YYY/ MM/ DD

TIME: HH: MM: SS

DATE/ TIME DISPLAY         ON

EXIT

ESC: RETURN

((: SELECT     ((: EDIT

ALARM            1-3

REC QUALITY                 HIGH

FRAME RATE                    30

REC DURATION(MIN)              1

EXIT

ESC:RETURN

((: SELECT  ((: EDIT

7    8       9        10  11  12         13                        14   15  16  17

VIDEO            1-5-1

BRIGHTNESS                          26

CONTRAST                       09

SATURATION                     19

HUE                                  25

RESET

TERMINATION                    ON

EXIT

MENU: ENTER   ESC:RETURN

((: SELECT     ((: EDIT

5

6

VIDEO            1-5-1

BRIGHTNESS              26

CONTRAST                14

SATURATION                19

HUE                       25

RESET

TERMINATION                 ON

EXIT

MENU: ENTER   ESC:RETURN

((: SELECT    ((: EDIT

CHANGE PASSWORD      1-5-6

PLEASE ENTER PASSWORD

X X X X

MENU: ENTER  ESC:RETURN

((: SELECT    ((: EDIT

NO       DATE    /    TIME

1     2002/10/02    18:00:00

2     2002/10/03    00:20:01

3     2002/10/03    12:05:31