Integrated High Speed Dome Camera

Outdoor Dome

Installation Guide

Version 2.1

Preface

The information given in this manual was current when published. The company reserves the right to revise and improve its products. All specifications are subject to change without notice.

Notice

This manual provides the installation information for the outdoor integrated high speed dome. To work with the dome cameras, any installer or technician must have the following minimum qualifications:

- A basic knowledge of CCTV systems and components

- A basic knowledge of electrical wiring and low-voltage electrical hookups

- Have read this manual completely

Copyright

Under copyright laws, the contents of this user manual may not be copied, photocopied, translated, reproduced or reduced to any electronic medium or machine-readable format, in whole or in part, without prior written permission of the company.

Important Information

Before proceeding, please read and observe all instructions and warnings in this manual. Retain this manual with the original bill of sale for future reference and, if necessary, warranty service. When unpacking your unit, check for missing or damaged items. If any item is missing, or if damage is evident, DO NOT INSTALL OR OPERATE THIS PRODUCT. Contact your dealer for assistance.

Regulation

This device complies with Part 15 of the FCC Rules. Operation is subject to the following two conditions:

(1) this device may not cause harmful interference, and (2) this device must accept any interference received, including interference that may cause undesired operation.

This symbol on the product or on its packaging indicates that this product shall not be treated as household waste in accordance with Directive 2002/96/EC. Instead it shall be handed over to the applicable collection point for the recycling of electrical and electronic equipment. By proper waste handling of this product you ensure that it has no negative consequences for the environment and human health, which could otherwise be caused if this product is thrown into the garbage bin. The recycling of materials will help to conserve natural resources.

For more details information about recycling of this product, please contact your local city office, your household waste disposal service or the shop where you purchased the product.

Compliance is evidenced by written declaration from our suppliers, assuring that any potential trace contamination levels of restricted substances are below the maximum level set by EU Directive 2002/95/EC, or are exempted due to their application. Since conditions of use are out of our control, Dynacolor Inc. makes no warranties, expressed or implied and assumes no liability in connection with the use of this information.

Warnings and Cautions

- Handle the camera carefully

Do not abuse the camera. Avoid striking, shaking, etc. The camera could be damaged by improper handing or storage.

- Do not disassemble the camera

To prevent electric shock, do not remove screws or covers. There are no user serviceable parts inside. Ask a qualified service person for servicing.

- Do not block cooling holes on the bracket

This camera has a cooling fan inside. Blocking the cooling holes leads to build up of heat the camera and may cause malfunction.

- Do not operate the camera beyond the specified temperature, humidity or power source ratings

Use the camera under conditions where temperature is between -30°C ~ 45°C (-22°F ~ 104°F), and relative humidity is below 90%.

- Do not use strong or abrasive detergents when cleaning the camera body

Use a dry cloth to clean the camera when it is dirty. In case the dirt is hard to remove, use a mild detergent and wipe the camera gently.

- Never face the camera towards the sun

Do not aim the camera at bright objects. Whether the camera is in use or not, never aim it at the sun or other extremely bright objects. Otherwise, the camera may be smeared or damaged.

Contents

1.	Introduction	5

2.	Standard Package Content	6

3.	Dome Setups and Cable Connection	7

3.1	Preparations for Dome Setups	7

3.2	Dome Setups	10

3.2.1	Switch Definition	10

3.2.2	Communication Switch Setting	10

3.2.3	Dome ID Setting	11

3.2.4	Dome Control Protocol Setting	12

3.3	Dome Cable Definition and Requirements	13

3.3.1	Cable Requirements	13

3.3.2	22-Pin Data Cable	14

3.3.2	22-Pin Connector Definition	14

3.3.4	RS-485 Connector Definition	15

3.3.5	Cable Wiring and Connection	16

4.	Dome Installation	18

4.1	Optional Accessories	18

4.2	Ceiling Mount with Straight Tube	23

4.3	Wall Mount	25

4.3.1	Wall Mounting with Gooseneck Tube	25

4.3.2	Mini Pendant Mount	26

4.3.3	Wall Box Mounting	27

4.4	Corner Mount	28

4.4.1	Corner Standard Mounting Plate	28

4.4.2	Corner Thin/Wide Box Mounting	30

4.5	Pole Mount	31

4.5.1	Pole Thin/Wide Direct Mounting	31

4.5.2	Pole Thin/Wide Box Mounting	32

5.	System Expansion	34

5.1	Connecting with Power Box	34

5.2	Data Formats Transforming	35

5.3	Signal Distribution Units	36

5.4	Coaxial Box	37

6.	System Integration	38

6.1	Using Pelco Keyboard	38

6.2	Using Philips Allegiant Keyboard	39

Appendix A: Technical Specification	40

1.	Introduction

With weather resistant feature, the Integrated High Speed Dome Camera is applicable to both indoor and outdoor installations. In addition, the dome camera is designed to deliver superb performance and durability with an intelligent and stylish housing that is suitable in any security and surveillance installation. Besides, the dome camera supports one cabling for easy installation. Large set of built-in protocols, including DynaColor, Pelco, VCL, Philips, AD-422 (Manchester), etc., provide connectivity to other suppliers’ surveillance systems.

General Operation Requirements:

A minimum of one control device is required for operation, such as a control keyboard, a DVR or a PC. The integrated high speed dome camera contains a built-in receiver that decodes commands from a control device.

Connect dome cameras to other devices, as shown in the diagram below, to complete a video surveillance system.

NOTE: To extend the network distance up to 1.2 km (4000 feet) and to protect the connected devices, it is highly recommended to place a repeater at the mid-point. However, a repeater may be needed in the network distance less than 1.2 km if the used cables are not the CAT 5, 24-gauge cables (see 3.3.4 RS-485 Connector Definition). Refer to the repeater’s manual for detailed information.

2.	Standard Package Content

Before proceeding, please check the box contains the items listed here. If any item is missing or has defects, DO NOT install or operate the product and contact your dealer for assistance.

| Dome Body | 50-cm Cable for Power Supply, Video and RS-485 | Optical Cover |
| --- | --- | --- |
| Lubricant | 50-cm, 13-pin Alarm Cable | M3×8 Screws, M5×8 Screw |
| Quick Guide | CD: User’s Manual & Installation Guide |  |

3.	Dome Setups and Cable Connection

Before installing or connecting the dome camera, please refer to the following sections and complete preparations for dome setups and various switch settings.

## 3.1	Preparations for Dome Setups

The section will illustrate the dome housing installation procedure of the outdoor dome equipped with a sunshield. Please follow the steps below to complete dome housing installation.

| STEP 1 Unpack the dome package and take out the dome body. |  |
| --- | --- |
| STEP 2 Rotate the top holder and take it off from the dome body. |  |
| STEP 3 Remove the 3 screws on the bottom of the sunshield. Then take off the sunshield from the dome body. |  |
| STEP 4 Set the dome on a flat table to keep it stable and then remove the protective cover and PE cloth. |  |
| STEP 5 Attach the dome cover to the dome body. Before doing that, apply some lubricant on the dome cover’s water-proof rubber to make the installation process smoother. |  |
| Note that the tiny protrusion on the dome cover must align with one of the four holes on the dome body. |  |
| STEP 6 Assemble the dome cover to the dome body by pressing the cover gently downward to the dome body with two hands on the side of the cover. |  |
| DO NOT press the cover as shown in the figure; this might cause damage to the dome body. |  |
| STEP 7 Screw the dome cover and body together. |  |
| STEP 8 Assemble the sunshield to the dome body and fix it with three screws. |  |
| STEP 9 Set the switches located on the bottom of the dome body. Refer to 3.2 Dome Setups for detailed information about various switch setting. |  |

## Dome Setups

Before connecting the dome camera to other devices of CCTV system, please complete the dome ID and various switch settings. These switches are located on the bottom of the dome camera.

### 3.2.1	Switch Definition

Please refer to the following figure and table for switch location and definitions.

| A | Reserved |
| --- | --- |
| B | Communication Switch |
| C | Dome ID Switch |
| D | Dome Control Protocol Switch |
| E | RJ-45 Connector (for IP Dome only) |
| F | 22-Pin Connector |
| G | ISP Connector (for FW upgrade) |

### Communication Switch Setting

The table below shows the function of each switch within the Communication Switch.

| Communication Switch | SW 1 | RS-485 Setting |
| --- | --- | --- |
|  | SW 2 |  |
|  | SW 3 | Termination |
|  | SW 4 | Line Lock |
|  | SW 5 | System Initialization (for upgrade) |
|  | SW 6 | Reserved |

RS-485 is the interface that communicates the dome camera and its control device; for this reason, the RS-485 setup of the dome and the control device must be the same. The RS-485 default setting is half-duplex (see the diagram follows). Please do not change the default setting without qualified specialist or supplier’s notice. As for the SW 3 and SW 4, they are used for termination and Line Lock adjustment respectively. The SW 5 is mainly used when users want to restore the camera to the factory default status; moreover, once firmware upgrade is carried out, users also need to reset the SW 5 afterward.

| RS-485 Setting |
| --- |
| Half-duplex | Full-duplex |

### 3.2.3	Dome ID Setting

Please change the dome ID if there is more than one dome on the same installation site. Use the switch to change your speed dome ID by turning the arrow to the desired number respectively. For instance, if the dome ID is 123, the ID switch should be set as below.

NOTE: No two domes should be given the same ID, or communication conflict may occur.

Centesimal Digit  Decimal Digit    Single Digit

NOTE: The number “0” should locate upwards as shown in above diagram for correct switch definition.

### 3.2.4	Dome Control Protocol Setting

Define the protocol you are going to use basing on the devices of your surveillance system. Generally, use one protocol even the devices are provided from different manufacturers. Use the switch to set your dome control protocol and the baud rate. Refer to the table below and turn the arrow to choose a protocol for your speed dome.

| Switch No. | Protocol | Baud Rate |
| --- | --- | --- |
| 00 | VCL | 9600 |
| 01 | Pelco D | 2400 |
| 02 | Pelco P | 4800 |
| 04 | Chiper | 9600 |
| 05 | Philips | 9600 |
| 07 | DSCP | 9600 |
| 08 | AD422 | 4800 |
| 09 | DM P | 9600 |
| 11 | Pelco D | 4800 |
| 12 | Pelco D | 9600 |
| 13 | Pelco P | 2400 |
| 14 | Pelco P | 9600 |
| 15 | JVC | 9600 |
| 21 | Kalatel-485 | 9600 |
| 22 | Kalatel-422 | 4800 |

Select protocol: Pelco D, with switch no. 01 and baud rate 2400, for instance, the ID switch should be set as shown below.

Decimal Digit   Single Digit

NOTE: The number “0” should locate upwards as shown in the diagram above for correct switch definition.

## Dome Cable Definition and Requirements

For operation, the integrated dome camera requires the video cable to carry the video signals to the remote viewing site, power cable to power the dome and RS-485 data cable to carry commands from the control device.

### Cable Requirements

For operation, the integrated high speed dome cameras require video and data cables as described below:

- The video cable sends video signals to a remote viewing site. Using a coaxial cable to send video signals is recommended.

- RS-485 cable carries commands from a control device to the dome cameras. A CAT 5, 24 gauge cable is recommended.

- The power cable provides AC 24V power supply to the dome.

NOTE: Ensure power supply corresponds with the dome’s power requirement, or product impairment will occur. If any mistake happens, please contact with a qualified maintenance engineer.

### 3.3.2	22-Pin Data Cable

|  | Power Input | 3-Pin Terminal Block |
| --- | --- | --- |
|  | Video Output | BNC connector |
|  | RS485 Connector | 2 wires |
|  |  | 4 wires |

NOTE: Be careful not to pull the cables improperly during installation. Additionally, it is suggested to fasten the cables after cable connection is completed. Furthermore, when wiring the power cable, make sure the G/Y wire (Ground) inserted into the mid-pin of the terminal block.

### 22-Pin Connector Definition

With the 22-pin connector, installers can simply connect the power, video and RS-485 cables to the dome at once. Particularly, the alarm pins are serviceable for connecting alarm input and output devices, such as alarm sensors, sirens or flashing lights with the surveillance system. For the definition of each pin, please refer to the list below.

The 22-pin connector definition is listed as below.

| Pin | Definition | Cable |
| --- | --- | --- |
| 1 | AC 24-1/DC GND | 20AWG |
| 2 | ALM NC |
| 3 | AC 24-2/DC 12(+) | 20AWG |
| 4 | ALM NO |
| 5 | FG | 20AWG |
| 6 | ALM COM |
| 7 | T+ | 24AWG |
| 8 | R- |  |
| 9 | T- |  |
| 10 | R+ |  |
| 11 | ISOG |
| 12~19 | ALM-1~ALM-8 |
| 20 | ALM GND |
| 21 | VGND | 24AWG |
| 22 | Video |  |

NOTE: For alarm connection, please refer to section 3.3.5 Cable Wiring and Conneciton.

### 3.3.4	RS-485 Connector Definition

RS-485 is the interface that communicates the dome camera and its control device. Please connect the control keyboard to the speed dome through the terminal block. The recommended cables for RS-485 communication are CAT 5 cables; maximum cable length for over 24-gauge wire is 4000 feet (1219 meters). If the total cable length exceeds 4000 feet, using a repeater to maintain the signals is recommended. Please refer to the figure and table below for pin defination and wiring.

| Pin | Corresponding Pins (22-Pin Connector) | Definition |
| --- | --- | --- |
| 1 | 7,10 | T+, R+ (D+) |
| 2 | Reserved |  |
| 3 | Reserved |  |
| 4 | Reservied |  |
| 5 | 8,9 | T-, R- (D-) |

### 3.3.5	Cable Wiring and Connection

Users may need to do cable wiring when: (1) Connecting self-provided cords to the connector housing instead of using the equipped data cable or (2) Connecting alarm input and output devices. The table follows will illustrate the way to wire cords into the connector housing. Please refer to 3.3.2 22-Pin Connector Definition for the exact position of each cord.

| Insert the terminal into the pin holes on the connector housing, with the hook outward, as indicated in the figure. |  |
| --- | --- |
| To unlock the terminal, press the hook, as indicated in the figure, with a proper tool and pull it out gently. |  |
| Connect the 22-pin connector to the dome camera. |  |

# 4.	Dome Installation

Basing on user’s installation environments, the dome can be installed on ceiling, on wall or on pole. In the following section, various dome installation accessories, installation methods and installation procedures will be described in detail.

## 4.1	Optional Accessories

Dome Camera Accessories

Sunshield White Color, Height: 135.5 mm (5.3 inches); Diameter: 261.6 mm (10.3 inches); 0.3 kg (0.7 lbs)

Vandal Proof (Transparent) /PMMA (Transparent)/Smoke Cover Diameter: 152mm (6 inches)

Security Screw Set (equipped with Vandal Proof Cover)

Power Adapter 77H07-A1015 (Input: 100~115VAC/Output: 24VAC 36VA) 77H07-A2015 (Input: 220~230VAC/Output: 24VAC 36VA) 77H07-A1030 (Input: 100~115VAC/Output: 24VAC 72VA) 77H07-A2030 (Input: 220~230VAC/Output: 24VAC 72VA)

Mounting Accessories

Gooseneck Tube White Color, Iron, 298×385 mm (11.73×15.56 inches) ; 2.1 kg (4.6 lbs) Supplied with rubber washer-8×1, pendant tube washer×1, spring washer-8×1 and waterproof rubber×1, M8*12 screw×1.

Mini Pendant Mount White/Ivory; 184×104×115.2 mm (7.24×4.09×4.54 inches) Supplied with rubber washer-8×1, pendant tube washer×1, spring washer-8×1 and M8*12 screw×1.

Straight Tube White, Iron, Height: 250/500 mm (9.8/19.7 inches) ,Diameter: 50 mm (2 inches) 1 kg (2.2 lbs) / 1.8 kg (4 lbs), Supplied with rubber washer-8×1, pendant tube washer×1, spring washer-8×1 and waterproof rubber×1, M8*12 screw×1.

Corner Standard Mounting Plate White, 222(L)×204(W)×117(D) mm (8.7×8×4.6 inches); 2 kg (4.4 lbs); Supplied with washer-8×4, spring washer×4, M8*20 screw×4, M8 nut×4.

Corner Thin Box White/Ivory, 300(L)×164(W)×222(D) mm (11.8×6.5×8.7 inches); 3 kg (6.7 lbs); Supplied with washer×4, M8*16 screw×4 and spring washer×4.

Corner Wide Box White/Ivory; 232(L)×234(W)×210(D) mm (9.1×9.2×8.3 inches); 2.7 kg (6 lbs); Supplied with washer×4, M8*16 screw×4 and spring washer×4.

Pole Thin Box White/Ivory; 291(L)×136(W)×245(D) mm (11.5×5.3×9.5 inches); 3.1 kg (6.9 lbs); Supplied with M8*16 screw×4, washer×4, spring washer×4, stainless steel straps×4.

Pole Wide Box White/Ivory, 270(L)×166(W)×155(D) mm (10.6×6.5×6.1 inches); 3.2 kg (7.1 lbs); Supplied with M8*16 screw×4, washer×4, spring washer×4, stainless steel straps×4.

Pole Thin Direct Mount White/Ivory, 232(L)×136(W)×60(D) mm (9.1×5.4×2.4 inches); Diameter: 112~140 mm (4.4~5.5 inches); 0.7 kg (1.6 lbs); Supplied with stainless steel straps×4, M8*16 screw×4, washer×4.

Pole Wide Direct Mount White/Ivory, 270(L)×170(W)×60(D) mm (10.6×6.7×2.4 inches); Diameter: 112~130 mm (4.4~5 inches); 1 kg (2.2 lbs); Supplied with stainless steel straps×4, M8*16 screw×4, washer×4, spring washer×4

Wall Box Mounting Ivory, 270(L)×166(W)×95(D) (10.6×6.5×3.7 inches); 2.2 kg (4.84 lbs); Supplied with M8*16 screw×4, washer×4, spring washer×4

Stainless Steel Straps For fixing Pole Direct Mounting/ Pole Box on the pole. Length: 700 mm (27.5 inches); Width: 0.63”; 0.02 kg (0.04 lbs)

Stainless Strap Cutter For tension, cut and crimp stainless steel straps. 1.4 kg (3.1 lbs) Suitable for straps width: 1/2”, 5/8”, 3/4”

Other Application Accessories

Repeater/Converter D77R1: RS-485/RS-232 Repeater D77R2: RS-232 between RS-485/RS-422 D77R3: Bi-phase to RS-485/RS-422

D77R1 D77R2 D77R3

Power Box White, 186.5×147 mm (7.3×5.8 inches); 2.6 kg (5.8 lbs) P1030 (Input: 110~115VAC/Output: 24VAC 72VA) P2030 (Input: 220~230VAC/Output: 24VAC 72VA)

Signal Distribution Units Relay control codes to speed dome cameras. Dimension: 432×44×90 mm (17×17.32×35.43 inches)

Coaxial Box Transmit video and RS-485 control signals via one BNC line. Dimension: 100×90×28 mm (3.93×3.54×1.1 inches)

Front View Rear View

4.2	Ceiling Mount with Straight Tube

The straight tube is available in different length: 25 cm and 30 cm.

Items Needed:

- Dome Camera

- Straight Tube and other equipped items (optional accessory)

- Screws and Screw Anchors for fixing the straight tube onto the ceiling (not supplied)

Tools Needed:

- Tool for drilling

- Tool for screwing

Follow the steps to mount the dome with the straight tube.

      - Ensure that the ceiling can support the weight of the dome camera and straight tube.

      - Make a cable entry hole on the ceiling.

      - Fix the Straight Tube to the ceiling with proper screws and screw anchors (not supplied).

      - Thread the cables through the straight tube and the top holder.

      - Fix the top holder to the straight tube with the supplied screws and washers. Then adjust the waterproof rubber to the junction of straight tube and top holder.

      - Connect the cables to the dome camera. Then attach the dome to the top holder and fix them with the supplied screw.

Ceiling Mount: Straight Tube + Waterproof Rubber

## 4.3	Wall Mount

## 4.3.1	Wall Mounting with Gooseneck Tube

The following figures show how cables run through the tube in different ways.

| Cables exposed | Cables recessed |
| --- | --- |

Items Needed:

- Dome Camera

- Gooseneck Tube and other equipped items (optional accessory)

- Screws and Screw Anchors for fixing the gooseneck tube on wall (not supplied)

Tools Needed:

- Tool for drilling

- Tool for screwing

Follow the steps to mount the dome with the gooseneck tube.

      - Make a cable entry hole on the wall to recess the cables. Otherwise, cables can be threaded through the cable entry hole on the tube.

      - Fix the Gooseneck Tube on the wall with proper screws and screw anchors (not supplied).

      - Thread the cables through the gooseneck tube and the top holder.

      - Fix the top holder to the gooseneck tube with the supplied screws and washers. Then adjust the waterproof rubber to the junction of straight tube and top holder.

      - Connect the cables to the dome camera. Then attach the dome to the top holder and fix them with the supplied screw.

Wall Mount: Gooseneck Tube + Waterproof Rubber

### 4.3.2	Mini Pendant Mount

Follow the steps to mount the dome with the Mini Pendant Mount.

Items Needed:

- Dome Camera

- Mini Pendant Mount and other equipped items (optional accessory)

- Screws and Screw Anchors for fixing the Mini Pendant Mount (not supplied)

Tools Needed:

- Tool for drilling

- Tool for screwing

- Make a cable entry hole on the wall to recess the cables. Otherwise, users could push up the cable entry board on the Mini Pendant Mount’s mounting plate to place the cables, as shown in the photo below.

- To avoid insects entering the pendant mount, you could block the cable entry hole with the supplied sponge in two ways. See the illustrations below.

- Thread the cables through the Mini Pendant Mount and fix the pendant mount on the wall with proper screws and screw anchors (not supplied).

4)	Thread the cables through the top holder and fix it to the Mini Pendant Mount with the supplied screws and washers.

5)	Connect the cables to the dome camera. Then attach the dome to the top holder and fix them with the supplied screw.

### 4.3.3	Wall Box Mounting

Items Needed:

- Dome Camera

- Gooseneck Tube and other equipped items (optional accessory)

- Wall Box (optional accessory)

- Screws and Screw Anchors for fixing the wall box on wall (not supplied)

Tools Needed:

- Tool for drilling

- Tool for screwing

Follow the steps to mount the dome with the gooseneck tube and wall box.

1)	Fix the Wall Box on wall with proper screws and screw anchors (not supplied).

2)	Fasten the gooseneck tube on the wall box with the supplied screws and washers.

3)	Thread the cables through the gooseneck tube and the top holder.

- Fix the top holder to the gooseneck tube with the supplied screws and washers. Then adjust the waterproof rubber to the junction of straight tube and top holder.

- Connect the cables to the dome camera. Then attach the dome to the top holder and fix them with the supplied screw.

Wall Box Mount: Wall Box Mount + Gooseneck Tube + Waterproof Rubber

## 4.4	Corner Mount

### 4.4.1	Corner Standard Mounting Plate

With the corner mounting plate and gooseneck, the dome can be mounted on corner wall.

Items Needed:

- Dome Camera

- Gooseneck Tube and other equipped items (optional accessory)

- Corner Standard Mounting Plate (optional accessory)

- Screws and Screw Anchors for fixing the Corner Standard Mounting Plate on corner wall (not supplied)

Tools Needed:

- Tool for drilling

- Tool for screwing

Follow the steps below to mount the dome camera with the corner standard mounting plate and gooseneck tube.

      - Make a cable entry hole on the wall to recess the cables. Otherwise, cables can be threaded through the cable entry hole on the tube.

      - Fix the Corner Standard Mounting Plate on corner wall with proper screws and screw anchors (not supplied).

      - Attach the gooseneck tube to the fixed mounting plate with the supplied screws and washers.

      - Thread the cables through the gooseneck tube and the top holder.

      - Fix the top holder to the gooseneck tube with the supplied screws and washers. Then adjust the waterproof rubber to the junction of straight tube and top holder.

      - Connect the cables to the dome camera. Then attach the dome to the top holder and fix them with the supplied screw.

Corner Wall Mount: Corner Standard Mounting Plate + Gooseneck Tube + Waterproof Rubber

### 4.4.2	Corner Thin/Wide Box Mounting

The corner thin/wide box is designed to be installed with a gooseneck tube.

Items Needed:

- Dome Camera

- Gooseneck Tube and other equipped items (optional accessory)

- Corner Thin/Wide Box (optional accessory)

- Screws and Screw Anchors for fixing the Corner Thin/Wide Box on corner wall (not supplied)

Tools Needed:

- Tool for drilling

- Tool for screwing

Follow the steps to mount the dome with the corner box and gooseneck tube.

      - Make a cable entry hole on the wall to recess the cables. Otherwise, cables can be threaded through the cable entry hole on the tube.

      - Fix the Corner Thin/Wide Box on corner wall with proper screws and screw anchors (not supplied).

      - Attach the gooseneck tube to the fixed corner box with the supplied screws and washers.

      - Thread the cables through the gooseneck tube and the top holder.

      - Fix the top holder to the gooseneck tube with the supplied screws and washers. Then adjust the waterproof rubber to the junction of straight tube and top holder.

      - Connect the cables to the dome camera. Then attach the dome to the top holder and fix them with the supplied screw.

Corner Box Mounting: Corner Thin/Wide Box + Gooseneck Tube + Waterproof Rubber

## 4.5	Pole Mount

### 4.5.1	Pole Thin/Wide Direct Mounting

The dome can be installed on a pole with a thin/wide direct mounting accessory and a gooseneck.

Items Needed:

- Dome Camera

- Gooseneck Tube and other equipped items (optional accessory)

- Pole Thin/Wide Direct Mounting (optional accessory)

- Stainless Steel Straps (optional accessory)

Tools Needed:

- Stainless Strap Cutter

- Tool for screwing

Follow the steps below to mount the dome camera with the pole direct mounting and gooseneck.

      - Fasten the Pole Thin/Wide Direct Mounting on a pole with equipped stainless straps.

      - Fix the gooseneck tube on the pole direct mounting with the supplied screws and washers.

      - Thread the cables through the gooseneck tube and the top holder.

      - Fix the top holder to the gooseneck tube with the supplied screws and washers. Then adjust the waterproof rubber to the junction of straight tube and top holder.

      - Connect the cables to the dome camera. Then attach the dome to the top holder and fix them with the supplied screw.

Pole Direct Mount: Pole Thin/Wide Direct Mounting +Gooseneck Tube + Waterproof Rubber

### 4.5.2	Pole Thin/Wide Box Mounting

Items Needed:

- Dome Camera

- Gooseneck Tube and other equipped items (optional accessory)

- Pole Thin/Wide Box(optional accessory)

- Stainless Steel Straps (optional accessory)

Tools Needed:

- Stainless Strap Cutter

- Tool for screwing

Follow the steps to mount the dome camera with the pole box and gooseneck tube.

      - Fasten the Pole Thin/Wide Box on a pole with equipped stainless straps.

      - Fix the gooseneck tube on the pole box with the supplied screws and washers.

      - Thread the cables through the gooseneck tube and the top holder.

      - Fix the top holder to the gooseneck tube with the supplied screws and washers. Then adjust the waterproof rubber to the junction of straight tube and top holder.

      - Connect the cables to the dome camera. Then attach the dome to the top holder and fix them with the supplied screw.

Pole Box Mount: Pole Thin/Wide Box + Gooseneck Tube + Waterproof Rubber

# 5.	System Expansion

## 5.1	Connecting with Power Box

A power box contains a 24V AC adapter, two terminal blocks (for communication and power) and one alarm board. With an IP66 case, the Power Box is ideal for outdoor installation environment. Two models are available: 100~115V AC power input (P1030) and 220~230V AC (P2030). Additionally, users can either connect one dome camera to one power box and to Internet or to other control devices (DVR, Control Keyboard and monitors), as shown in the diagrams below. For more detailed information, please refer to the power box user’s manual.

Connecting the Dome to the Power Box and Internet

Connecting the Dome to the Power Box and Various Control Devices

NOTE: One power box can only be connected to one outdoor dome camera subject to voltage restriction. In addition, up to two indoor dome cameras are allowed to be used with one power box.

## 5.2	Data Formats Transforming

To integrate other surveillance devices with the high speed dome cameras or to extend the distance of communications, users could employ three kinds of repeater/converter, as shown below. With the advanced circuit design, these repeaters/converters offer 1KVrms isolation voltage and surge protection capability. The exiting network can be protected by the repeaters/converters. Up to 10 devices are allowed to connect to one repeater/converter. For detailed information, please refer to the repeater/converter user’s manual.

| D77R1 RS-485/RS-232 Repeater | D77R2 RS-232 between RS-485/RS-442 | D77R3 Bi-Phase to RS-485/RS-422 |
| --- | --- | --- |

D77R1:	Extend the distance of RS-485 or RS-422 communications

D77R2:	Either Bridge RS-232 equipments to a RS-485 or RS-422 network or bridge RS-485/RS-422 equipments to a RS-232 network

D77R3:	Bridge Bi-Phase equipments to a RS-485 or RS-422 network

## 5.3	Signal Distribution Units

The RS-485 Signal Distribution Unit (SDU) is designed to relay control codes to speed dome cameras. It is capable of communicating with cameras up to 1.0 kilometers away. Additionally, the SDU can be installed in either “star” or “daisy chain” configuration with up to 160 cameras (see the diagrams below). Its versatile installation configuration makes an easy integration into expanding surveillance systems. For more information, please refer to the SDU user’s manual.

Star Configuration

Daisy Chain Configuration

## 5.4	Coaxial Box

The Coaxial Box is a low-cost solution to long distance connection between dome cameras and controlling devices (e.g. DVR and keyboard). It simplifies the work of wiring by transmitting video and RS-485 control signals via one BNC line, so that to bring users economical benefits. The following is the coaxial box application diagram. For more information, please refer to the coaxial box user’s manual.

# 6.	System Integration

The dome camera is allowed to be integrated into other suppliers' surveillance systems with large set of built-in protocols. Refer to the following sections for more information.

## 6.1	Using Pelco Keyboard

The speed dome camera can be controlled through a Pelco keyboard which built in with D protocol and P protocol. Please follow the instruction to manipulate our speed dome by a keyboard with D and P protocols.

| Function | Instruction |
| --- | --- |
| Set Preset | Number key + press and hold <Preset > button for three seonds. |
| Go Preset | Number key + <Preset> to command a dome camera to go to a specific preset position. |
| Display or hide an OSD menu | 7 7 <Preset> |
| Move the cursor in OSD menu | Move the cursor up/down/right/left by pushing the joystick up/down/right/left respectively |
| <ENTER> | 7 7 <Preset> |
| Reset the dome camera | 7 8 <Preset> |

Cable Definition (P Protocol Keyboard to PTZ Camera)

Cable Definition (D Protocol Keyboard to PTZ Camera)

## 6.2	Using Philips Allegiant Keyboard

The dome cameras can be integrated into Philips Allegiant systems through D77R3 repeaters. Please follow the instructions to control dome cameras through Philips Allegiant systems.

Symbol Definition

| <shot> | Command dome cameras to go to specific preset position. |
| --- | --- |
| <set> | Set preset position. |

Special Function

| 7 6 <set> | Exit OSD menu directly. |
| --- | --- |
| 7 7 <set> | 1. Display or hide OSD menu. 2. Virtual key to send an ENTER command when OSD is displayed. |
| 7 8 <set> | Reset doma camera. |
| <Iris Open> | Send an ENTER command when OSD is displayed. |

Control Dome Camera Using Allegiant Keyboard

- User can move the cursor left/right/up/down through pushing joystick

left /right/up/down.

- Some differences for ENTER command.

User cannot send ENTER command directly. User can send a ENTER command through “ 7 7 <Set> “.

# Appendix A: Technical Specification

|  | Items | R Model | C Model | F Model | K Model | U Model |
| --- | --- | --- | --- | --- | --- | --- |
| CAMERA |
|  | Effective Pixels | NTSC | 380k |
|  |  | PAL | 440k |
|  | Horizontal Resolution | NTSC | 480 TV lines |
|  |  | PAL | 480 TV lines |
|  | Scanning Area | Progressive 1/4" CCD | 1/4" CCD ExView | 1/4" CCD ExView | Progressive 1/4" CCD | 1/4" CCD ExView |
|  | Scanning System | PAL, NTSC |
|  | Synchronization | Internal / Line Lock |
|  | Video Output | 1.0 Vp-p / 75, BNC |
|  | S/N Ratio (AGC OFF) | More than 49dB |
|  | Minimum Illumination | 1 lux | 1.0 lux | 0.7 lux; 0.01lux (B/W) | 0.1 lux; 0.02lux (B/W) | 0.07 lux; 0.01lux (B/W) |
|  | Focal Length | 4~88 mm | 4.1~73.8 mm | 3.6~82.8 mm | 3.5~91 mm |
|  | Zoom Ratio | 22× optical zoom | 18× optical zoom | 18× optical zoom | 23× optical zoom | 26× optical zoom |
|  | Digital Zoom | ×1 ~ ×12 variable |
|  | Focus Mode | Auto / Manual |
|  | White Balance | Auto / Manual |
|  | Iris Control | Auto / Manual |
|  | Electronic Shutter | NTSC | 1/60~1/30k sec. | 1/1~1/10k sec. | 1/2~1/30k sec. | 1/1~1/10k sec. |
|  |  | PAL | 1/50~1/30k sec | 1/1~1/10k sec | 1/1.5~1/30k sec | 1/1~1/10k sec |
|  | AGC control | Auto / Manual |
|  | Back Light Compensation | On / Off |
| OPERATION |
|  | Built-in Protocol | DynaColor, Pelco, VCL, Philips, AD-Manchester, AD-422, JVC, Kalatel, etc. |
|  | Multi-Language OSD | English, French, German, Italian, Japanese, Polish, Portuguese, Russian, Spanish |
|  | Pan Travel | 360° endless |
|  | Tilt Travel | -10°~100° | -10°~190° |
|  | Manual Speed | 1°~90°/s |
|  | Presets | 256 |
|  | Preset Accuracy | Pan | 0.225° |
|  |  | Tilt | 0.45° |
|  | Preset Speed** | Pan | 5°~400°/s, High Resolution (Both D&E Type Motor) |
|  |  | Tilt | 5°~400°/s, Standard Resolution (D Type Motor). 5°~400°/s, High Resolution (E Type Motor) |
|  | Cruise | 1 |
|  | Sequence | 8 |
|  | Auto Pan | 4 |
|  | Privacy Mask | - | 24 | 24 | 8 | 24 |
|  | Pan & Tilt Speed Proportional to Zoom Ratio | Yes | Yes | Yes | Yes | Yes |
|  | P/T/Z Auto-Restoring | Yes | Yes | Yes | Yes | Yes |
|  | Auto Turn Around | Yes | Yes | Yes | Yes | Yes |
|  | Zone Title | Yes | Yes | Yes | Yes | Yes |
|  | Home Function | Yes | Yes | Yes | Yes | Yes |
|  | Digital Flip | - | - | Yes | Yes | Yes |
|  | Digital Slow Shutter | - | - | Yes | Yes | Yes |
|  | Motion Detection | - | Yes | Yes | - | Yes |
|  | Wide Dynamic Range | - | - | - | Yes | - |
|  | Day/Night: IR Cut Filter | - | - | Yes | Yes | Yes |
|  | Alarm Input | 8 |
|  | Alarm Output | 1 |
| GENERAL |
|  | Environment | Outdoor |
|  | Controller Interface | RS-485 |
|  | Operating Temperature | -30°C~45°C (-22°F~104°F) |
|  | Water Proof Standard | IP 66 Standard |
|  | Dimension | ∅262×305mm (10.4x12 Inches), with sunshield |
|  | Weight | 5.8 kg (12.9 lbs) |
|  | Power Source | AC 24V |
|  | Power Consumption | 30 W / 65 W (with Heater) |
|  | Regulatory | CE, FCC, IP66 |

**There are D&E motors, differentiated by the type of motors of high speed dome cameras and presents various “Preset Speed” and resolutions. Standard Resolution: 800 steps/circle. High Resolution: 1600 steps/circle.

# Comments

n

description of the SW 5 has been revise

# Text boxes

Cable Entry Board

Sponge

Sponge

Mounting Plate