# UltraMix H.264 NVR

# Setup Guide

# Package Content

Inspect the packaging carton. Make sure the UltraMix H.264 NVR is properly delivered. Remove all items from the box and make sure the box contains the following items.

| UltraMix H.264 NVR | Power Adaptor | Power Cord |
| --- | --- | --- |
|  | USB Mouse | Setup Guide | Software CD |

# Front Panel

| 1 | Camera LED | Orange: The power is supplied by the camera itself. Green: The power is supplied by the PoE switch at the rear panel. |
| --- | --- | --- |
| 2 | P.Max | It lights up when power supply of PoE ports reaches the maximum. |
| 3 | UpLink LED | It lights up when the NVR is connecting with the Internet. |
| 4 | Power LED | It lights up when the power is on. |
| 5 | Alarm LED | It lights up when an alarm is triggered. |
| 6 | Record LED | It blinks when videos are being recorded. |
| 7 | Network LED | It blinks when the PoE Switch and the NVR keep good communication. |
| 8 | USB Ports *3 | The USB ports allow users to connect external USB devices to the NVR, such as a USB ThumbDrive® or a USB mouse. |

# Rear Panel

| 1 | USB Ports *2 | The USB connectors are provided for users to connect external USB devices to the NVR. Note that USB 2.0 only port cannot connect the USB mouse or the USB keyboard. |
| --- | --- | --- |
| 2 | Main Monitor (HDMI) | A HDMI connector is provided for connection to a displaying device that transfers data digitally to show the best video quality. |
| 3 | Alarm I/O & RS485 | The unit provides alarm I/O and RS-485 ports that offer users the flexibility required to connect the NVR to the other devices. The pin definition is listed below. |
| 4 | LAN 10/100M (RJ-45) | The NVR is capable of networking and it allows the videos to be viewed over the LAN network or the internet via internet browsers. |
| 5 | PoE ports | The PoE ports offer direct connections to 6 IP cameras. Note that only Nx Series of the IP cameras can be “plug and play”. |
| 6 | Power Jack | Connect the power adaptor and the power cord shipped with the NVR. Use of other power supply may cause overloading. |

# Pin Definition of Alarm I/O & RS-485:

|  | Pin | Definition | Pin | Definition |
| --- | --- | --- | --- | --- |
|  | 0 | Alarm In 1 | 5 | RS485 D+ |
|  | 1 | Alarm In 2 | 6 | RS485 D− |
|  | 2 | Alarm In 3 | 7 | Alarm Out NO |
|  | 3 | Alarm In 4 | 8 | Alarm Out COM |
|  | 4 | Ground | 9 | Alarm out NC |

# Power On the NVR

Please follow the proper power on procedures to avoid damaging the NVR.

- Connect all necessary components, e.g. network cable, IP cameras, monitor and USB mouse, before power on the NVR.

- Check the type of power source before plugging in the power cord to the NVR. The acceptable power input is between AC110V ~ AC240V.

# Login the System:

Once the NVR is correctly powered on, first login to operation the NVR.

- Select the administrator account “admin” to login. Enter the preset password “1234”.

- It is strongly suggested to change the password to prevent unauthorized access.

# Function Bar Icons

The Function Bar will be displayed at the bottom and the functional icons are listed as below.

| Item | Icon | Description | Item | Icon | Description | Item | Icon | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 |  | Menu | 4 |  | PTZ Control | 7 |  | System Info |
| 2 |  | Mode | 5 |  | Playback | 8 |  | Camera Setup |
| 3 |  | Search | 6 |  | Monitor Mode |  |  |  |

Another group of display icons shown on the right of the Menu icon are the status icons. Refer to the following chart for their descriptions.

| Item | Icon | Description | Item | Icon | Description |
| --- | --- | --- | --- | --- | --- |
| 1 |  | Record | 9 |  | Disk Error |
| 2 |  | Event Record | 10 |  | Disk Full |
| 3 |  | Lock | 11 |  | Disk Overheat |
| 4 |  | Zoom | 12 |  | No Disk |
| 5 |  | Pause @ Playback mode | 13 |  | Disk Almost Full |
| 6 |  | Forward Playback Speed: 1x, 2x, 4x, 8x, 16x, 32x | 14 |  | HDD Usage |
| 7 |  | Backward Playback Speed: 1x, 2x, 4x, 8x, 16x, 32x | 15 |  | User’s Authority Level |
| 8 |  | End of Video | 16 |  | Guest |

NOTE: Items #9~#14 will only be displayed when the circular recording mode is OFF.

# Basic Setup

Enter the OSD main menu to setup some basic configuration of the NVR. The basic configuration can be set via either the NVR or NVRRemote, the remote software.

# Enter OSD Main Menu:

- Click on the Menu icon in the Function Bar and select <Menu> to enter the OSD main menu.

# Date / Time Setting:

Follow the steps below to setup date/time before the recording starts. Refer to the User’s Manual for advanced setup of Time Sync function.

- Select <Date/Time> in System menu.

- Select date or time, and adjust the value by clicking on the UP/DOWN buttons.

- The new date and time settings take effect after the changes are confirmed.

# Language Setting:

If users wish to change the language of the NVR system, follow the steps below.

- Select <Language> in System menu.

- Click on the DOWN buttons to choose the preferred language.

# Network Setup

Configure the LAN setup for the NVR to properly function with Ethernet connection.

- From OSD main menu, select <System > ( <Network Setup>, set the <LAN Select> item to <LAN>, and enter <LAN Setup>.

- For DHCP users, set the DHCP to <ON>. The IP address, Netmask, Gateway and DNS settings are retrieved from network servers. DHCP is dynamic that the settings change from time to time.

- For Non-DHCP users, set the DHCP to <OFF>. IP address, Netmask, Gateway and DNS settings must be set. Please obtain the information from the network service provider.

- To change the IP address, Netmask, Gateway and DNS value, click on the <Num> button to display the number pad and input users’ preferred setting values.

- When the settings are completed, click on the <X> icon on the top-right corner to exit.

# Monitor Mode

The NVR provides Standard and Portrait viewing modes in full-screen, 4-windows and 6-windows layouts. Refer to the following for operations how to change viewing modes.

- Click on the Monitor Mode icon in the function bar to change between Standard or Portrait modes.

- Click on MODE repeatedly to select a preferred display layout.

# Refer to the User’s Manual for more detail.

# IP Camera Connection

# IP Camera Setup via Plug and Play Connection:

Please follow the steps below to configure IP cameras connected to the NVR via PoE ports.

- Click on the Camera Setup icon in the function bar and the following menu will be displayed.

| Camera Search |  |
| --- | --- |
|  | Nx Series |  |
| Brand ***** ***** ***** | Model ***** ***** ***** | IP Address 192.168.6.111 192.168.6.112 192.168.6.113 | MAC Address **:**:**:**:**:** **:**:**:**:**:** **:**:**:**:**:** |
| IP: 192.168.6.111 | CH01 CH02 CH03 CH04 CH05 CH06 |  |
| Camera Setting |
|  | PnP | Activate | Protocol | IP Address | More |
| ‧CH01 | On | Off | Nx Series | 192.168.50.*** |  |
| ‧CH02 | On | Off | Nx Series | 192.168.50.*** |  |
| ‧CH03 | On | Off | Nx Series | 192.168.50.*** |  |
| ‧CH04 | On | Off | Nx Series |  |  |
| ‧CH05 | On | Off | Nx Series |  |  |
| ‧CH06 | On | Off | Nx Series |  |  |

- Click on Device Setup icon <>. Users can directly configure the settings of the IP Camera. Note that Device Setup is ONLY available for Nx Series.

- Click on Event Setup icon <> at the right of Camera Setting. Users can configure event setting of each channel. Four event types, <Vloss>, <Motion>, <AlmIn> and <AlmOut>, are included in Event Setup. Note that <AlmIn> and <AlmOut> ONLY support CH1~CH4.

# NOTE: For more details about Device Setup, please refer to User’s Manual.

# IP Camera Setup via Internet Connection:

If users need to connect and setup IP cameras via network, please follow the steps below.

- First select the type of IP camera model on the top-right. Click on Search icon <> at the top-right corner. The NVR will search the selected models in the same LAN.

- Under PnP, switch <On> to <Off> at the preferred channel.

- Click on a preferred IP camera in the list. Then click on the channel button whose PnP function is <Off>.

- Under Activate, switch <Off> to <On> at the selected channel. The NVR will begin to connect the selected IP camera.

- If users need to configure the advanced setup, click on IP Camera Setup icon <> before activating the IP camera.

- To further configure Device Setup and Event Setup, users can refer to the steps from previous subsection.

# NOTE: For more details about IP Camera Setup and Device Setup, please refer to User’s Manual.

# Indication Icons of Connection Status:

# The indication icons are next to the channels at camera setting. Users can see the connection status of IP cameras while setting up the IP cameras.

| Icon | Description | Icon | Description |
| --- | --- | --- | --- |
| ‧ | Successful Connection | ‧ | Connecting IP Camera |
| ‧ | No IP camera setup for the channel | ‧ | Failed Connection |

Status Icons of IP Camera:

# The table below describes the connection status of IP camera at Live mode.

| Icon | Description | Icon | Description |
| --- | --- | --- | --- |
|  | Connecting IP Camera |  | Successful Connection |
|  | Failed Connection |  | Resolution Oversize |
|  | No Connection |  |  |

# PTZ Control

When an IP Dome Camera is connected, users can click on the PTZ Control icon in the function bar to operate the PTZ Control function right at the NVR site. Note that the IP Dome Protocol and the IP Dome ID must be set correctly in <IP Camera Setup>. Refer to the previous section for more details.

# Control Buttons in Dome Camera Control Panel:

| Icon | Description | Icon | Description | Icon | Description |
| --- | --- | --- | --- | --- | --- |
|  | Iris Close |  | Iris Open |  | Focus Far |
|  | Focus Near |  | Zoom Out |  | Zoom In |
|  | Set / Go Preset Points |  | Return to Live Mode |  | Auto Focus |
|  | Move the Lens to the Left |  | Move the Lens to the Right |  | Move Up the Lens |
|  | Move Down the Lens |  |  |  |  |

# NOTE: There is no reaction for functions that are not supported by the Dome Cameras.

# Basic Playback Operation

# Search By Time:

- Click on the Search icon in the Function Bar to enter the Search menu.

- Click on “From” and playback will start from the specified “From” time.

- Click on “End” and playback will start from the specified “End” time.

- Click on “Select” and choose date or time. Click on the UP/DOWN buttons to adjust the values.

- Click on <Begin Playback> to start playing back recorded video of the selected time.

NOTE: If no available recorded video matches the specified time and date, the unit starts to playback from the next available video.

Calendar Search:

- Click on the Search icon in the Function Bar to enter the Search menu.

- Click on <Calendar Search> and a calendar will show up.

- Select any date shown in underlined font, which means recording data are available. The table shown on the left will display available videos of each channel within the selected date.

- The videos are classified into four categories: Normal, Motion, Alarm In and Video Loss, shown as four different tabs on the top.

- Then select a preferred time from the time bar. Alternatively, specify the values of date/ hour/ minute/ second under <Select> on the right.

- The video preview windows will playback previews of the selected time. Users can click on the preview window to instant playback the video.

- The <From> and <End> buttons allow users to playback video from the beginning or end of the database.

- Click on <Begin Playback> to start playing back the selected video.

# Search by Event:

- Click on the Search icon in the Function Bar to enter the Search menu.

- Adjust date / time next to <From> and <End> under <Search By Event> to specify time range of the event search.

- Select the channels and/or event types to be filtered in the event search.

- Click on <Event List> to list the event video of the selected channels.

- The list displays each event by date, time, triggered camera and event type. The latest recorded event video will be listed on the top. Click on the <X> icon on the top-right corner to exit.

- Click on the buttons at below to see the previous or next pages of the Event List. Click on the selected event record to playback the event video.

NOTE: The event list displays only the first 1024 events; as some events are deleted, others are displayed.

# Playback Controls of Control Panel Buttons:

| Icon | Description | Icon | Description |
| --- | --- | --- | --- |
|  | Time Frame of the Previous Day |  | Time Frame of the Next Day |
|  | Backward Playback: Click repeatedly to increase speed by 1×, 2×, 4×, 8×, 16×, or 32×. |  | Forward Playback: Click repeatedly to increase speed by 1×, 2×, 4×, 8×, 16×, or 32×. |
|  | When the playback is paused, click on this icon to do Step Backward. |  | When the playback is paused, click on this icon to do Step Forward. |
|  | Pause Playback |  | Change Viewing Mode |
|  | Search Menu |  | Return to Live Mode |

# System Info

The System Info page will be shown as below. There are mainly three parts: the brief info of IP cameras at top-left, the connection status of IP cameras at top-right, and the brief system info at the bottom. Users can click on any IP camera icon at top-right to show its brief info at top-left.

The link to IP camera icons will be displayed in four different colors.

- Green: This indicates good connection to the IP camera.

- Red: This represent the connection to the IP camera is failed.

- Blue: This means the NVR is trying to connect to the IP camera.

- Grey: There is no IP camera setup for the channel.

# Click on the CLOSE button to exit the System Info page.

# Connect the NVR via the Remote Software

# Setup Requirements:

- Make sure the PC is connected to the Internet.

- Obtain IP address of the UltraMix H.264 NVR. To check the NVR’s IP address, click on the Menu icon in the Function Bar and select <Menu> to enter the OSD main menu. Select <System> ( <Network Setup> ( <LAN Setup> ( <IP> to check the IP.

# Changing Internet Setting:

- Start the IE; select <Tools> from the main menu of the browser, then <Internet Options> and then click the <Security> tab.

- Select <Trusted Sites> and click <Sites> to specify its security setting.

- Uncheck “Require server verification (https:) for all sites in this zone”. Type the IP address of the unit in field and click <Add> to add this website to the zone.

- In the Security Level area, click <Custom Level>. Under <ActiveX controls and plug-ins>, set all items to <Enable> or <Prompt>.

- Click <OK> to accept the settings and close the <Security Settings> screen.

# Using the Remote Software:

- Start the IE and enter the IP address of the UltraMix H.264 NVR in the address bar.

- The ActiveX controls and plug-ins dialog will show up twice for confirmation; click <YES> to accept ActiveX plug-ins. The NVRRemote plug-ins will be downloaded and installed on the PC automatically when the connection is successfully made.

NOTE: Do not enter any leading “0” characters in the address, for example, “192.068.080.006” should be entered “192.68.80.6”.

NOTE: If the default trigger port 80 is changed to another one, take port 81 for example, users should enter the IP address as “192.68.80.6:81”.

- Version verification starts automatically to verify whether NVRRemote was installed. This process may take up to 30 seconds.

- When the software is completely downloaded and installed, the Login Screen is displayed.

- Enter username and password. The default username and password is admin and 1234.

The following picture shows the display window of the NVRRemote.

Refer to the table below for brief description of functional items:

| Item | Description | Item | Description |
| --- | --- | --- | --- |
| 1 | Instant Recording | 9 | Search Event List |
| 2 | Smoothen the Image | 10 | Capture Snapshot |
| 3 | Audio On/Off | 11 | 4:3 Viewing Aspect |
| 4 | Select Camera | 12 | HDD Health Status |
| 5 | Display Mode | 13 | Playback Control |
| 6 | View Live Camera | 14 | Select Picture Size |
| 7 | Playback Video | 15 | Bandwidth – Normal/Dual Stream |
| 8 | Setup Menu |  |  |

# For more information on NVRRemote, see User’s Manual.

# NVRRemote Playback

# Playback Remote Video:

- Click <Play> on the main window toolbar, and then <Remote Playback> tab.

- The <From> and <To> on top of the screen display the date and time from which recorded video is available for playback.

- Choose <Playback> in <Select> field for playback recorded video.

- Select the date and time of the segment to play back from the <Start> field. Users can change the date and time either by typing desired numbers directly or using the arrow buttons.

- Click <OK> to start the playback, or click <Close> to abort.

# Playback Local *.drv File:

- Click <Play> on the main window toolbar, and then <Local Playback> tab.

- Click <Open> and the file selection screen is displayed. Select the *.drv video file to playback and click <OK>.

- Click <OK> to start the playback, or click <Cancel> to abort.

- View the video playback using the Playback controls.

- To end the playback, click <Live> to return to live video.

# Playback Local *.avi Files:

- Start the windows media player or other media player from <Start> menu (or any other possible access).

- Select <File> and then <Open>.

- Select the wanted *.avi file, and click <Open>.

NOTE: The *.avi files for each channel are stored separately. Therefore, the video can be played back in single channel, full screen mode only.

# Playback Event Video:

- Click SEARCH on the main window toolbar. The Event List appears.

- Scroll through the Event List and highlight the interested events.

- Double-click on the desired event to view the event video.

# Playback Controls: