This Quick Guide is a reference for users to install and operate the Camera quickly, and thus only provides basic information on the Camera’s various setting and operation. Before attempting to connect, configure and operate the Camera, please read its Installation Guide, User’s Manual and OSD Menu thoroughly.

System Configuration

Switch Definition

Indoor                                      Outdoor

| Item | Definition | Remark |
| --- | --- | --- |
| A | I/O | ALARM I/O |
| B | ID | Dome Camera ID Setup DIP Switch |
| C | BNC | BNC Video Output |
| D | SETTING | Communication Switch Setting |
| E | Protocol | Camera Control Protocol Setting |
| F | RS485 | RS485 Connector |
| G | AC24V Connector | Power connector |

Please kindly check the pin definition of the Power Connector listed above before connecting to the power source. The AC24V power source should be connected to the first and third pin. The unit might be damaged with wrong connection.

Communication Switch Setting

The table below shows the function of each switch within the Communication Switch on the Camera’s back plate.

| Communication Switch | SW 1 | RS-485 Setting |  | RS-485 Setting |
| --- | --- | --- | --- | --- |
|  | SW 2 |  |  | Half-duplex | Full-duplex |
|  | SW 3 |  |  |  |  |
|  | SW 4 |  |  |  |  |
|  | SW 5 | Reserved |  |  |  |
|  | SW 6 | Reserved |  |  |  |

ID Setting

Please assign an ID number to a Camera if there is more than one Camera in the same network. The camera’s ID can be setup using the 10-bit ID Dip Switch, which is located on the Camera’s back plate. If the Camera’s ID number is 6, for instance, the ID switch SW 2 and SW 3 should be set to “ON” and the rest should be set to “OFF” as shown below. Dip Switch configuration for ID No. 0~10 are listed in the table below. To complete ID setups, please refer to the User Manual.

| ID No. | Switch Setting |
| --- | --- |
|  | SW 1 | SW 2 | SW 3 | SW 4 | SW 5 | SW 6 | SW 7 | SW 8 | SW 9 | SW 10 |
| 0 | OFF | OFF | OFF | OFF | OFF | OFF | OFF | OFF | OFF | OFF |
| 1 | ON | OFF | OFF | OFF | OFF | OFF | OFF | OFF | OFF | OFF |
| 2 | OFF | ON | OFF | OFF | OFF | OFF | OFF | OFF | OFF | OFF |
| 3 | ON | ON | OFF | OFF | OFF | OFF | OFF | OFF | OFF | OFF |
| 4 | OFF | OFF | ON | OFF | OFF | OFF | OFF | OFF | OFF | OFF |
| 5 | ON | OFF | ON | OFF | OFF | OFF | OFF | OFF | OFF | OFF |
| 6 | OFF | ON | ON | OFF | OFF | OFF | OFF | OFF | OFF | OFF |
| 7 | ON | ON | ON | OFF | OFF | OFF | OFF | OFF | OFF | OFF |
| 8 | OFF | OFF | OFF | ON | OFF | OFF | OFF | OFF | OFF | OFF |
| 9 | ON | OFF | OFF | ON | OFF | OFF | OFF | OFF | OFF | OFF |
| 10 | OFF | ON | OFF | ON | OFF | OFF | OFF | OFF | OFF | OFF |

RS485 Connector Definition

Please refer to the illustrations below for RS485 connector definition before wiring.

| RS485 Connector | SW 1 | R- |
| --- | --- | --- |
|  | SW 2 | GND |
|  | SW 3 | R+ |
|  | SW 4 | T- |
|  | SW 5 | T+ |

Camera Control Protocol Setting

Refer to the table below and select one set of protocol and baud rate you would like to use basing on the control device; then adjust the protocol switch on the Camera’s back plate. For instance, to setup protocol Pelco D/ Baud Rate 2400, which is Switch No. 01, the Switch SW 1 should be set to “ON”, and the rest Switches should be set to “OFF”.

|  | Switch No. | Protocol | Baud Rate | Switch Setting |
| --- | --- | --- | --- | --- |
|  |  |  |  | SW 1 | SW 2 | SW 3 | SW 4 | SW 5 | SW 6 |
|  | 00 | VCL | 9600 | OFF | OFF | OFF | OFF | OFF | OFF |
|  | 01 | Pelco D | 2400 | ON | OFF | OFF | OFF | OFF | OFF |
|  | 02 | Pelco P | 4800 | OFF | ON | OFF | OFF | OFF | OFF |
|  | 04 | Chiper | 9600 | OFF | OFF | ON | OFF | OFF | OFF |
|  | 05 | Philips | 9600 | ON | OFF | ON | OFF | OFF | OFF |
|  | 07 | DSCP | 9600 | ON | ON | ON | OFF | OFF | OFF |
|  | 08 | AD422 | 4800 | OFF | OFF | OFF | ON | OFF | OFF |
|  | 09 | DM P | 9600 | ON | OFF | OFF | ON | OFF | OFF |
|  | 11 | Pelco D | 4800 | ON | ON | OFF | ON | OFF | OFF |
|  | 12 | Pelco D | 9600 | OFF | OFF | ON | ON | OFF | OFF |
|  | 13 | Pelco P | 2400 | ON | OFF | ON | ON | OFF | OFF |
|  | 14 | Pelco P | 9600 | OFF | ON | ON | ON | OFF | OFF |
|  | 15 | JVC | 9600 | ON | ON | ON | ON | OFF | OFF |
|  | 21 | Kalatel-485 | 9600 | ON | OFF | ON | OFF | ON | OFF |
|  | 22 | Kalatel-422 | 4800 | OFF | ON | ON | OFF | ON | OFF |
|  | 23 | Panasonic | 19200 | ON | ON | ON | OFF | ON | OFF |

Power Connector Definition

Please refer to the illustrations below for power connector definition before wiring.

|  | SW 1 | AC24V_1 |
| --- | --- | --- |
|  | SW 2 | GND |
|  | SW 3 | AC24V_2 |

Alarm I/O Connector Definition

When cabling, please refer to the pin definition as below for alarm system alarm.

|  | SW 1 | ALARM_OUT_NO_1 | SW 7 | ALARM_OUT_COM_2 |
| --- | --- | --- | --- | --- |
|  | SW 2 | ALARM_OUT_NC_1 | SW 8 | GND |
|  | SW 3 | ALARM_OUT_COM_1 | SW 9 | ALARM_IN_4 |
|  | SW 4 | GND | SW10 | ALARM_IN_3 |
|  | SW 5 | ALARM_OUT_NO_2 | SW11 | ALARM_IN_2 |
|  | SW 6 | ALARM_OUT_CN_2 | SW12 | ALARM_IN_1 |

Integrated High Speed Dome Camera

Quick Guide

Ver 1.3

# Text boxes

RS-485 Connector

Video Output