HDCopy Tool User’s Manual

Ver 1.1

Content

1. HDCopy Tool Introduction	3

2. Install EXT2IFS to Your PC	3

3. Converting Process	4

4. Start with HDCopy Tool Software	6

# 1. HDCopy Tool Introduction

The HDCopy Tool is used to convert the data stored in the Hard Disk Drive of DynaGuard 500 series DVR.

For some specific reasons, users may need to view the stored data on the Personal Computer; and HDCopy Tool is quite useful under this situation. It helps to convert the raw data into a *.drv file or a *.avi file, and these two file formats are both acceptable for the Windows PCs. A *.drv file can be viewed using the software DVRPlayer. DVRPlayer can be found in the CD-ROM attached in the package; A *.avi file can be directly viewed through Windows Media Player.

# 2. Install EXT2IFS to Your PC

EXT2IFS, an installed File System Driver, allows you to run a Linux System on Windows System. If you are a Windows user, then you need to install EXT2IFS to your PC before you start using HDcopytool to convert the raw data.

To get the software EXT2IFS, you can visit http://uranus.it.swin.edu.au/~jn/linux/ext2ifs.htm and download EXT2IFS. A detailed description about the software also can be found on the website.

# 3. Converting Process

The following sections guide you step by step to convert the raw data into the Windows-acceptable files.

- Download EXT2IFS to your PC through above website address.

- Remove the HDD from DynaGuard 500 series DVR and install the removed HDD into your PC. When done, reboot the PC.

- Extract and Launch EXT2IFS Setup Wizard.

- Click <Step1> sheet, and then choose <Install to SystemRoot> and <Start drive on boot> options. When done, click <Install Drive> button.

- Click <Step2b> sheet. Click <Drive> to assign each partition a drive.

- After the assignments are made, click <Save Assignments> button.

- Click <Step3> sheet. Then click <Start Drive> button.

- After last step is done, reboot the PC for the changes to take effect. The HDD will be added into your PC’s database after rebooting.

# 4. Start with HDCopy Tool Software

The following sections guide you to convert the image files, which had been saved in the HDD, into *.drv file or *.avi file. If converted into *.drv file, you need DVRPlayer the software to playback the video (DVRPlayer can be found in the attached CD). If converted into *.avi file, you can read this file using Windows Media Player directly.

To convert the image files, follow these steps:

- Insert the CD, which is attached in the DVR package, to your PC. Find “HDCopy Tool” software, and copy and save it into you PC.

- Start HDCopy Tool software by clicking on its icon.

- Click <Select> button and choose the drive where a partition had been assigned to it (Refer to Page 4, Point 5).

- Select the folder which you want its contained image files to be converted, and click <OK> button.

- After folder selection, click <Save as> and choose the destination where you want to save the converted file.

- Name and select the wanted format for the file. Then click <Save>.

- Choose the record that wanted to be converted.

  - If want to convert Normal data, click on <Normal> button. Then configure the Start Time / End Time and Channel boxes. After configuration, click <OK> to start converting.

  - If want to convert Event data, click on <Event> button. And then click to select the wanted Event file.

- Click <OK> button to start converting.