Step1: VPON Firmware upgrade to MOVS beta version. (Important!)

- It is suggested to upgrade firmware from “Remote”. (Use http://aa.bb.cc.dd/revise.htm to do upgrade VPON firmware. Where aa.bb.cc.dd means VPON IP address.)

- Upgrade "system.bin.en.14_32mb_patch" First. VPON will reboot twice to be ready.

- After finishing step (3), upgrade "system.bin.en.14_0_MOVS_std_32mb". VPON will reboot again to be ready.

- Select correct camera standard as NTSC or PAL under “System setup/Camera setting” to get right camera video.

Step2: Install MO-SOFT on your mobile phone.

- Open the Internet Browser of your mobile phone.

- Link to wap.mo-soft.com/wap page.

- Select the language of your area.

- Select “Product”, and find “VPON”.

- Select to download “mo-vpon” program.

- After download, find the program on your mobile phone and install.

- After complete, select the program to start.

- Enter the IP and Account of VPON, also serial number of MO-SOFT if you have.

- You can start to remote VPON on your mobile phone.