FW1.4.0 POS Record release note

New Feature:

- POS Text Recording / POS Event Recording function under “Record Schedule” Menu. Support under OSD, GUI, Web interface.

- Support Pre-alarm Recording and Weighted Recording.

- DVR will start to record for a pre-defined period when POS text shown on the screen.

- Min. record period for POS Text Recording and POS Event Recording: 30 seconds.