WebMonitor Plus Hardware Specification (Revised) :

| Audio Input / Output | Support half duplex audio I/O Two audio output Three audio input |
| --- | --- |
| Video Input / Output | Support NTSC/PAL Six video output Six video input with video standard auto detection |
| Compression | Support H.263, M-JPEG, JPEG video compression format |
| Resolution | Image size: 320x240 (JPEG), 176x144 (H.263) 24 bits true color |
| Performance | Up to 10 frame/second (JPEG), 10 frame/second (H.263) |
| Typical Bandwidth | 100K Byte/second (JPEG) 5K Byte/second(H.263) |
| Hardware | 32bits CPU, 8MB DRAM 2MB Flash-ROM for firmware One MODEM Port One Camera Control Port Four digital input and four output for surveillance Front panel LEDs power indication and status display Built-in a pre-configured mini web server |
| Installation | Assign IP address, ISP phone number, login name, password |
| System Compatibility | All PC running Navigator 3.0 or later |
| Protocols | Support TCP/IP, PPP, HTTP |
| Connectors | One 10BaseT Ethernet port Six RCA connectors for video input One DB9 Male Connector for configuration and Modem connection One DB9 Male Connectior for Camera control One DB9 Female Connector for video output Three RCA connectors for audio input Two RCA connectors for audio output Two 8-pins Mini-DIN connectors for digital input/output |
| Power Supply | 25 watts power consumption, 90-264VAC, 47-63HZ |
| Size | 300mm(W) x 165mm(D) x 55mm(H) |
| Accessory | RS232 Cable Power Cord Manual System Configuration Software Mini-DIN to Terminal Block Cable DB9-to-six-RCA Cable |

WebMonitor Plus Software Functions

|  | 線上切換中英文網頁, 用一般瀏覽器即可查看 可同時查看所有攝影機影像 可針對特定區域影像做 ZOOM-IN 效果 線上選擇想要查看的攝影機影像 可多人同時查看 即時顯示系統時間 即時擷取單張影像存檔 4組警報輸出入接點, 可外接各類偵測器材 提供Netscape Plug-ins, 提升低頻寬環境的 Frame Rate 可搭配 OYO Viewer, 做為整合性即時監控系統 可以URL連接到任何網站, 不須開發任何程式 系統設定值查看 Ethernet 設定值 (MAC Address, IRQ, I/O base...) TCP/IP 設定值 (IP Address, DNS, Gateway, Subnet Mask) COM Port Status 攝影機設定 亮度 ,明暗對比, 色彩飽和度 , 彩度 , 影像品質 即時查看設定結果 設定 WebMonitor 系統時間 設定監視系統參數 其他系統設定 TCP/IP stack configuration(IP Address,DNS, Gateway, Subnet Mask) ISP configuration (Phone Number,Login Name,Password,Modem Baud Rate) Authenticate configuration (User Name, Password) Set Video Compression Algorithm |
| --- | --- |

## WebMonitor Plus Software Functions

- On-line alter Home pages of English version or Chinese version, view the video with Netscape Navigator

- View the video of all cameras connected to WebMonitor at the same time

- ZOOM-IN the video of a specified portion

- On-line choose to view the video of a certain camera

- Multi-users login in at the same time

- Show the real time clock of the system

- Provide Netscape Plug-Ins to increase Frame Rate in the narrow bandwidth environment

- Use OYO Viewer ( a proprietary software) to apply at the integrated real time surveillance system

- Connect to any Web Site by URL, don’t need to develop any program

- Check the system setting

- Ethernet configuration (MAC Address, IRQ, I/O base…)

- TCP/IP configuration (IP Address, DNS, Gateway, Subnet Mask)

- COM Port Status

- Configure the cameras attribution

- Brightness, Contrast, Color Situation, Hue, Quality of the video

- Real time check the configuration

- Set WebMonitor’s system time

- Set surveillance system parameters

- Other system configuration

- TCP/IP stack configuration (IP Address, DNS, Gateway, Subnet Mask)

- ISP configuration (Phone number, Login Name, Password, Modem, Baud Rate)

- Set Video Compression Algorithm

OYO Viewer 1.0 Software Functions:

- 透過MODEM 撥接WebMonitor

提供驅動MODEM程式介面, 撥接連線PC和WebMonitor

- 快速撥號/電話簿

提供快速撥號, 記憶已撥接電話號碼.

電話簿功能, 可管理撥接電話號碼.

- 密碼限制查看權限

撥接連線完成後, 需通過密碼檢查才能查看WebMonitor

- 可同時查看所有攝影機影像

- 線上選擇想要查看的攝影機影像

- 即時顯示系統時間

- 即時擷取影像存檔

擷取螢幕顯示之影像存檔, 大小及影像品質與螢幕顯示相同

- 事件驅動自動回撥傳回影像

GPI輸入點可驅動WebMonitor自動回撥功能, 撥接連線完成後, WebMonitor會將事件發生瞬間以後的影像傳回OYO Viewer. 之間若有異常斷線, OYO Viewer會主動再撥接連線將影像取回

- 遠方傳回影像自動存檔

傳回影像會自動存檔, 以供播放

- 播放遠方傳回影像

提供影像播放功能可播放任何已存檔之影像

- 線上系統設定

可線上設定亮度 ,明暗對比, 色彩飽和度 , 彩度 , 影像品質

Viewer Functional Block Diagram

# Text boxes

Viewer Application

Video

Decoder

VGA	Driver

COMM

Driver

DDRAW

Win32

COMM	API

Viewer Kernel DLL